Source	MARKET NEWS
Date	09/18/2017
Time	05:19:41 AM

Company	 I-Minerals Inc.
Title	Produces its 
Best Ever Metakaolin





    CDNX Symbol: IMA











Press Release





I MINERALS INC ("IMA-V;IMAHF-0")
- Produces its Best Ever Metakaolin

I-Minerals lnc. (the "Company")announces that further to the
Company's press release of August 29, 2017, it has received results of
ASTM C618-15 testing from CTL Thomson in Denver, CO of the various
metakaolin products produced using the flash calcination technologies
of FLSmidth in Allentown, PA. The key test is the water requirement
measured as a percentage of the control samples with 115% of control
the acceptable maximum. Four samples representative of calcining
temperatures of 700, 750, 800 and 850 C were sent for testing and all
fell in the range of 108-110% of control and hence handily met the ASTM
C618-15 water demand specifications.

"As part of the last several pilot plants, we have experimented
with particle sizes and other inputs," stated Thomas Conway President
and CEO of I-Minerals Inc. "However, this metakaolin, produced using
the flash calcination technology, has created the best combination of
strength, lowest water demand and color. As noted in our press release
of August 29, initial testing of the use of hydrocyclones to make the
clay/sand separation generated a cleaner cut resulting in higher clay
recovery. Hence not only are we making the best metakaolin we ever
have, but the hydrocyclone technology stands to increase metakaolin
production with potential to modestly reduce both CAPEX and OPEX."

With respect to the 28-day Strength Activity Index (%) number, the
minimum threshold to achieve to meet the ASTM C618-15 standard is 75.
The four samples sent for testing resulted in values from 86.4-94.3 %
and are expected to increase with additional time. For comparative
purposes fly ash, the most common pozzolan, generally demonstrates
strength numbers in the mid-80s, although there is variability across
fly ash products.

"These results indicate we can make a pozzolan at least as good as
high-quality fly ash," continued Conway. "With fly ash becoming scarcer
as coal fired electric plants shift to gas or are shut down, a
consistent supply of quality pozzolans is becoming increasingly
challenging. Water demand is the test that inhibits the success of many
natural pozzolans and meeting the specifications bodes very well for
the market opportunities for our metakaolin in the Pacific Northwest.
Having a high quality metakaolin alongside our best in class K-spar,
our world class halloysite and the highest SiO(sub)2(/sub), lowest iron
quartz in the Pacific Northwest positions the Company very well as we
push forward towards eventual production of these high-quality
minerals."

A. Lamar Long, CPG, is a qualified person ("QP") for I-Minerals
Inc. and has reviewed and approved the contents of this release

About I-Minerals Inc.

I-Minerals is developing multiple deposits of high purity, high
value halloysite, quartz, potassium feldspar and kaolin at its
strategically located Helmer-Bovill property in north central Idaho. A
2016 Feasibility Study on the Bovill Kaolin Deposit led by GBM
Engineers LLC, who were responsible for overall project management and
the process plant and infrastructure design, including OPEX and CAPEX
calculated an After Tax NPV of US$249.8 million with a 25.8% After Tax
IRR. Initial CAPEX was estimated at $108.3 million with a 3.7 year
After Tax payback. Other engineering services were provided by HDR
Engineering, Inc. (all environmental components; hydrology /
hydrogeology; road design); Tetra Tech, Inc. (tailings storage facility
design); Mine Development Associates (mine modelling; ore scheduling;
mineral reserve estimation); and SRK Consulting (U.S.) Inc. (mineral
resource estimation). The project has received mine and water permits
from the State of Idaho.

I-Minerals Inc.

Per: "Thomas M. Conway"

Thomas M. Conway, President & CEO

This News Release includes certain "forward looking statements"
within the meaning of the United States Private Securities Litigation
Reform Act of 1995. Without limitation, statements regarding potential
mineralization and resources, exploration results, and future plans and
objectives of the Company are forward looking statements that involve
various risks. Actual results could differ materially from those
projected as a result of the following factors, among others: changes
in the world-wide price of mineral market conditions, risks inherent in
mineral exploration, risk associated with development, construction and
mining operations, the uncertainty of future profitability and
uncertainty of access to additional capital.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
NEWS RELEASE

Contact Information:

Contact:

Barry Girling
877-303-6573 or 604-303-6573 ext. 102
Email: info@imineralsinc.com
Or visit our website at www.imineralsinc.com

Paul J. Searle
Investor Relations
877-303-6573 or 604-303-6573 ext. 113
Email: psearle@imineralsinc.com
______________________________
_______________________________________________
TSX Venture closing price for IMA-V
Date: 2017/09/15
Closing Price: 0.36
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1726000007TS11726000770-05190520170918