Source	MARKET NEWS
Date	09/18/2017
Time	07:04:43 AM

Company	 Tinka Resources Limited
Title	Drills 10.8 
Metres Grading 16.7% Zinc at South A





    CDNX Symbol: TK











Press Release





TINKA RESOURCES LTD ("TK-V;TKRFF-0")
- Drills 10.8 Metres Grading 16.7% Zinc at South Ayawilca
- Zinc Resource Update by November 2017

Tinka Resources Limited ("Tinka" or the "Company") is pleased to
announce assay results for an additional nine step-out drill holes from
the Company's 100%-owned Ayawilca zinc project in central Peru. Strong
zinc intercepts continue to be encountered at South Ayawilca and West
Ayawilca. An initial hole at the Chaucha area, about 1.5 kilometres
north of the Ayawilca resource, shows encouraging geology and this area
requires additional work. Tinka continues to expand the footprint of
the zinc mineralization at Ayawilca, with approximately 15,000 metres
in 44 holes drilled year-to-date at several prospective areas (Figure
1). Step-out drilling in the current program is expected to continue at
South Ayawilca until December.

The Company is also pleased to announce that it intends to update
the Ayawilca zinc resource estimation on completion of the two holes
now in progress at South Ayawilca (including sampling and assaying).
The resource update is expected to be completed by early November. RPA
Inc. of Toronto has been retained to complete the resource update and
the accompanying National Instrument 43-101 report.

Key Highlights of latest drill holes Hole A17-089 (South
Ayawilca):

//st

* 10.8 metres at 16.7 % zinc & 681 g/t indium from 218.6 metres depth,
including
* 1.8 metres at 35.9 % zinc & 1,248 g/t indium from 218.6 metres depth,
and
* 2.7 metres at 33.6 % zinc & 1,800 g/t indium from 222.5 metres depth;

//et

9.2 metres at 7.9 % zinc, 18 g/t silver & 60 g/t indium from 241.0 metres
depth.
Hole A17-083 (West Ayawilca):

//st

* 2.9 metres at 8.0 % zinc, 0.6 % lead & 61 g/t silver from 81.6 metres
depth;
* 10.2 metres at 3.0 % zinc, 0.7 % lead & 15 g/t silver from 268.0 metres
depth.

//et

Hole A17-085 (West Ayawilca):

//st

* 1.8 metres at 9.6 % zinc from 292.3 metres depth;
* 2.4 metres at 14.3 % zinc, 0.2 % lead & 18 g/t silver from 303.1 metres
depth.

//et

Dr. Graham Carman, Tinka's President and CEO, stated: "Our
ongoing drill program continues to expand the high grade zinc
mineralization at South Ayawilca and to grow the West Ayawilca zone
beyond the limits of the existing resource model. Following up on our
successful campaign so far, I am pleased to announce that Tinka is
planning an updated estimate of the zinc mineral resources at Ayawilca
by early November. This resource update will be a significant milestone
for the Company, and it will incorporate mineralization at the
high-grade South Ayawilca discovery. Importantly, drilling will
continue beyond this period as we test the southern and eastern
extensions of South Ayawilca for further high-grade discoveries."

Dr. Carman continued: "Tinka was recently awarded the title of
'Explorer of the Year Americas 2017' by the Mining Journal of London,
UK. We are very proud of this award as it brings with it recognition of
our achievements during the year. We believe there is much more value
to be added, as we advance towards a significant resource update and
continue to de-risk Ayawilca with additional studies including
metallurgical test work which will be reported late 2017. We also
believe there is more exploration upside to be unlocked as zinc
mineralization remains open in multiple directions."

See Table 1 for a summary of all significant zinc intercepts in
the 2017 drill program to date.

South Ayawilca area Mineralization at South Ayawilca remains open
to the south and southeast (Figure 2). Five holes from South Ayawilca
have assays pending (A17-093 through A17-097) and two holes are in
progress (A17-098 and A17-099). Holes A17-087 and A17-089 have some
very high grade zinc intercepts at the western end of South Ayawilca
where the prospective limestone appears to thin out (Figure 3).

West Ayawilca area New results from holes A17-083 and A17-085 have
expanded the mineralization at West Ayawilca to the northeast (Figure
4). Mineralization remains open in this direction, and further drilling
is planned in 2018.

Chaucha, Zone 3 and Valley target areas Tinka has now drilled its
first exploration holes into the Chaucha, Zone 3 and Valley target
areas, about 1.5 kilometres north of the Ayawilca zinc resources
(Figure 1). At Chaucha, two holes were successfully drilled to test a
discrete magnetic anomaly approximately 150 metres across. Drill hole
A17-086 intersected massive iron oxides (magnetite - hematite) and
pyrite over a down hole interval of 125 metres (from 57.50 to 181.80
metres) within a sub-vertical brecciated carbonate host rock. Although
there was no significant zinc mineralization we believe the abundance
of iron, a first for this style of mineralization at Ayawilca, could
indicate the presence of a large hydrothermal system nearby. More
drilling is planned in 2018, to better understand the significance of
the mineralization encountered. The second hole at Chaucha, A17-084,
tested outside the limit of the magnetic anomaly and did not intersect
significant mineralization.

At the Zone 3 area, hole A17-081 was stopped at 506 metres in
chlorite-altered limestone. The chlorite alteration is interpreted to
indicate a nearby mineralizing heat source. Results are pending for
hole A17-091, which also encountered strong chlorite alteration in a
fault zone. Given the high priority of the resource drilling, the
Company recently moved the drill rig from Zone 3 to South Ayawilca.
More drilling is planned for Zone 3 in 2018. At the Valley area,
results are pending for holes A17-090 and 092.

True thicknesses of the zinc intersections are estimated to be at
least 85% of the downhole thickness, except where otherwise noted in
footnotes to Table 1. All significant results of the 2017 program are
summarized in Table 1 with the strongest intercepts in bold text. Table
2 summarizes all drill collar information to date.

Maps attached: Figure 1: Geological map with 2017 drill holes and
targets; Figure 2: Drill hole locations at South, West and Central
Ayawilca; Figure 3: Longitudinal section of South Ayawilca; Figure 4:
Cross section of West Ayawilca;

NI 43-101 Technical Report: On June 29, 2016, Tinka filed an
independent National Instrument 43-101 Technical Report (the "NI 43-101
Technical Report") on the Mineral Resource Estimate for the Ayawilca
Property, Department of Pasco, Peru in support of the Company's news
release dated May 25, 2016. The NI 43-101 Technical Report was authored
by Mr. David Ross. P.Geo., of Roscoe Postle Associates Inc., who is an
independent "qualified person" as defined by National Instrument
43-101. The NI 43-101 Technical Report may be found under the Company's
profile on SEDAR at www.sedar.com and on the Company's website at
www.tinkaresources.com.

The qualified person, Dr. Graham Carman, Tinka's President and
CEO, and a Fellow of the Australasian Institute of Mining and
Metallurgy, has reviewed and verified the technical contents of this
release.

Table 1. Summary of 2017 Drill Results from Ayawilca by Area and
Date of Release

Table is available at
https://www.tinkaresources.com/news/tinka-drills-10-8-metres-grading-16-7-z
inc-at-south-ayawilca-zinc-resource-update-by-november-2017



//st
1 hole lost at 293.9 metres; wedged and completed as A17-056A to 376
metres depth

2 includes 0.6 m with no core recovery from 315.2 to 315.8 m; this interval
was given a zero
grade

3 includes 3.1 m with no core recovery from 198.8 to 201.9 m; this interval
was given a zero
grade

4 includes a silver assay cut at 1,000 g/t; actual assay in A17-056 was 0.2
m at 16,490 g/t Ag,
7.0% Zn & 6.9 % Cu from 287.1 m.

5 high grade vein intercepts with variable true thicknesses

6 includes 4.3 m of no recovery assumed zero grade

7 includes 1.7 m of no recovery assumed zero grade

Note: Assays are calculated using a zinc only cut-off grade of 2% over 6
metres

//et

Notes on sampling and assaying Drill holes are diamond HQ or
NQ size core holes with recoveries generally above 80% and often close
to 100%. The drill core is marked up, logged, and photographed on site.
The cores are cut in half at the Company's core storage facility, with
half-cores stored as a future reference. Half-core is bagged on average
over 1 to 2 metre composite intervals and sent to ALS or SGS
laboratories in Lima for assay in batches. Standards and blanks are
inserted into each batch prior to departure from Tinka's core storage
facilities. At the laboratory samples are dried, crushed to 100%
passing 2mm, then 500 grams pulverized for multi-element analysis by
ICP using multi-acid digestion. Samples assaying over 1% zinc, lead, or
copper and over 100 g/t silver are re-assayed using precise ore-grade
AAS techniques.

Table 2. Summary of Drill Collar Information (coordinates are in
UTM Zone 18S WGS84 datum)

//st

Drill Hole   Easting   Northing   Total       Elevation      Azimuth   Dip
depth (m)   (m)
A17-056      333046    8845062    293.9       4202           300       -75

A17-056A     333046    8845062    376.4       4202           300       -75

A17-057      333046    8845062    477.0       4202           300       -55

A17-058      332557    8845657    301.0       4299           040       -82

A17-059      332840    8845192    248.9       4209           120       -85

A17-060      333174    8845005    358.4       4218           300       -70

A17-061      333058    8844996    326.9       4191           290       -67

A17-062      333175    8845004    309.0       4218           000       -90

A17-063      333241    8845118    416.6       4229           310       -70

A17-064      333062    8844993    369.1       4191           290       -50

A17-065      333174    8845090    366.3       4225           300       -75

A17-066      333345    8845193    371.6       4211           310       -70

A17-067      333059    8844996    302.8       4190           120       -85

A17-068      333552    8845279    419.7       4185           310       -75

A17-069      333114    8845103    374.3       4210           300       -65

A17-070      333152    8845150    367.8       4230           310       -75

A17-071      333328    8845044    383.3       4202           310       -70

A17-072      333114    8845103    445.9       4233           300       -53

A17-073      334458    8846616    710.0       4024           210       -75

A17-074      332666    8845491    429.6       4124           015       -75

A17-075      333434    8845121    395.3       4201           310       -70

A17-076      333155    8845153    420.7       4230           310       -55

A17-077      332966    8845460    416.2       4243           130       -70

A17-078      333656    8845227    477.2       4174           310       -75

A17-079      332919    8845717    322.6       4223           310       -65

A17-080      332915    8845805    335.4       4220           310       -70

A17-081      334696    8846099    506.8       4151           190       -70

A17-082      333774    8847585    67.2        3922           290       -65

A17-083      332968    8845607    317.6       4216           310       -70

A17-084      333694    8847613    123.1       3938           300       -75

A17-085      332903    8845938    346.6       4250           310       -70

A17-086      333693    8847613    217.9       3938           300       -50

A17-087      333005    8844940    316.8       4160           290       -72

A17-088      332689    8846884    224.6       4163           170       -65

A17-089      333003    8844943    330.1       4160           325       -60

//et

On behalf of the Board,
"Graham Carman"

Dr. Graham Carman, President & CEO

About Tinka Resources Limited Tinka is an exploration and
development company with its flagship property being the 100%-owned
Ayawilca carbonate replacement deposit (CRD) in the zinc-lead-silver
belt of central Peru, 200 kilometres northeast of Lima. The Ayawilca
Zinc Zone has an Inferred Mineral Resource of 18.8 Mt at 5.9 % zinc,
0.2 % lead, 15 g/t silver & 74 g/t indium, and a Tin Zone Inferred
Mineral Resource of 5.4 Mt at 0.76 % tin, 0.31 % copper & 18 g/t silver
(May 25, 2016). A significant resource expansion drill program began in
February 2017 and is ongoing.

Forward Looking Statements: Certain information in this news
release contains forward-looking statements and forward-looking
information within the meaning of applicable securities laws
(collectively "forward-looking statements"). All statements, other than
statements of historical fact are forward-looking statements.
Forward-looking statements are based on the beliefs and expectations of
Tinka as well as assumptions made by and information currently
available to Tinka's management. Such statements reflect the current
risks, uncertainties and assumptions related to certain factors
including, without limitations, drilling results, the Company's
expectations regarding mineral resource calculations, capital and other
costs varying significantly from estimates, production rates varying
from estimates, changes in world metal markets, changes in equity
markets, uncertainties relating to the availability and costs of
financing needed in the future, equipment failure, unexpected
geological conditions, imprecision in resource estimates or metal
recoveries, success of future development initiatives, competition,
operating performance, environmental and safety risks, delays in
obtaining or failure to obtain necessary permits and approvals from
local authorities, community agreements and relations, and other
development and operating risks. Should any one or more of these risks
or uncertainties materialize, or should any underlying assumptions
prove incorrect, actual results may vary materially from those
described herein. Although Tinka believes that assumptions inherent in
the forward-looking statements are reasonable, forward-looking
statements are not guarantees of future performance and accordingly
undue reliance should not be put on such statements due to the inherent
uncertainty therein. Except as may be required by applicable securities
laws, Tinka disclaims any intent or obligation to update any
forward-looking statement.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release

Investor Information: www.tinkaresources.com, Rob Bruggeman,
1.416.884.3556, rbruggeman@tinkaresources.com; Company Contact: Mariana
Bermudez, 1.604.699.0202, info@tinkaresources.com ______________________________
_______________________________________________
TSX Venture closing price for TK-V
Date: 2017/09/15
Closing Price: 0.58
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1726000032TS11726001372-06591720170918