Source	MARKET NEWS
Date	09/25/2017
Time	06:52:51 AM

Company	 Taranis Resources Inc.
Title	Identifies New High Grade Gold Bearing Zone At T





    CDNX Symbol: TRO











Press Release





Identifies New High Grade Gold Bearing Zone At Thor Parallel To TheThor Ag Au 
Pb Zn Cu Deposit, Channel Samples 28.79 G/t Au / 3.72 mTrue Thickness 
--->@NEWS RELEASE
TARANIS RESOURCES INC ("TRO-V")
- Identifies New High-Grade Gold-Bearing Zone At Thor Parallel To
- The Thor Ag-Au-Pb-Zn-Cu Deposit, Channel Samples 28.79 G/t Au /
- 3.72 m True Thickness

Taranis Resources Inc. ("Taranis" or the "Company") is pleased to
update exploration activity related to its 100%-owned Thor project.

Excavation of ore for the gold pilot plant at Thor has uncovered
the continuation of high-grade gold mineralization at the SIF Zone in
an area now referred to as the SIF-Extension. The original SIF zone
occurs west of the main Ag-Au-Pb-Zn-Cu deposit within the top of an
anticline fold structure, but it is now known that the zone rolls onto
the west side of the anticline structure and continues to plunge
moderately (450) to the northwest.

Taranis will issue a separate News Release concerning the mining
activity, and gold recovery of the original SIF Zone once it has ceased
processing ore.

Channel Sampling

Excavation of the SIF-Extension below the mined-out SIF Zone has
allowed Taranis to complete nine lines of channel sampling across the
exposure, each representative of the true thickness of the zone. The
sampled exposure shows the true thickness of the zone, and all sampling
is directly taken on surface. ICP analyses are pending, and will be
released at a later date. Channel sample lines are spaced 1.5 m apart,
and are normal to the dip of the gold-bearing zone.

//st

---------------------------------------------------
|Channel Sample Line|True Thickness (m)|Gold (g/t)|
|-------------------------------------------------|
|1                  |1.98              |7.03      |
|-------------------------------------------------|
|2                  |1.28              |4.35      |
|-------------------------------------------------|
|3                  |2.10              |23.18     |
|-------------------------------------------------|
|4                  |3.26              |9.10      |
|-------------------------------------------------|
|5                  |2.93              |4.21      |
|-------------------------------------------------|
|6                  |3.72              |28.79     |
---------------------------------------------------

//et

SIF-Extension Geology

The SIF-Extension zone contains visible gold similar to broken ore
from the SIF Zone that is currently being processed in the gold pilot
plant. In contrast to the main Thor Ag-Au-Pb-Zn-Cu deposit that
includes abundant sulphide minerals, the SIF and SIF-Extension Zones
consist of massive quartz with brecciated textures, and most distinctly
a reddish iron oxide mineral that forms prominent gossans. Visible gold
is commonly found in the zone, and it occurs with small amounts of
magnetite, pyrite and within vuggy cavities in the rock.

The SIF-Extension is up to 3.72 m thick, and folded into an
"s-shaped" fold plunging steeply to the northwest, and dipping to the
southwest along the Sharon Creek / Broadview Formation contact
identical to the main Thor Ag-Au-Pb-Zn-Cu deposit. This is consistent
with a VMS deposit setting where it is common to find gold distal to
the base-metal enriched core of the deposit, but within the same
stratigraphic horizon.

The stratabound nature of the mineralization indicates that the
SIF-Extension gold target is potentially very large, and it has been
subsequently modified by extensive folding and north-northwest
high-angle faulting. The southwest side of the outcrop exposes a
southwest dipping fault that appears to abruptly truncate the
SIF-Extension zone, and opens the possibility that the zone is
faulted-off from a currently unlocated gold zone. Additional evidence
for this is shown by a thickening of the zone and increasing gold
content towards the fault.

Geophysical Survey Tracing SIF Extension to Northwest

Previous geophysical surveys (2014) identified a strong VLF
conductor in this area that extends for 120m to the northwest under a
landslide infilling a valley, and this area has not been tested with
any diamond drilling. Taranis has completed a detailed grid over the
northwest continuation of the zone and has identified a strong
conductive feature that is related to the newly discovered SIF
Extension.

Quality Control

Samples are delivered by Taranis via courier to MS Analytical Labs
in Langley, British Columbia. MS Analytical Labs is an ISO-9001:2008
certified analytical laboratory. The Company inserts external standards
every 10th sample for quality control in addition to the stringent
internal checks completed at MS Analytical. Samples are dried, crushed,
split and pulverized. Analysis for gold is done by 30 gram fire assay
with ICP and gravimetric finish.

Qualified Person

John Gardiner (P.Geol.) is the Qualified Person on the Thor
Project, and supervised the preparation of the scientific and technical
disclosure in this News Release.

About Taranis Resources Inc.

Taranis is an exploration company focused on the development of
its 100%-owned Thor project in southeast British Columbia. The
Company's mandate is to recognize mineral deposits early in the
exploration cycle that can be developed through intelligent exploration
and business alliances. For additional information on Taranis or its
Thor project, please visit our website at www.taranisresources.com.

Taranis currently has 55,451,716 shares issued and outstanding
(63,376,716 shares on a fully-diluted basis).

TARANIS RESOURCES INC.
Per:    John J. Gardiner (P. Geol.),
President and CEO

For further information contact:

//st

---------------------------------------------
|John J. Gardiner                         ||
|14247 West Iliff AvenueLakewood, Colorado| |
|Phone: (303) 716-5922                    | |
|Cell: (720) 209-3049                     | |
|johnjgardiner@earthlink.net              | |
---------------------------------------------

//et

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
NEWS RELEASE.

This News Release may contain forward looking statements based on
assumptions and judgments of management regarding future events or
results that may prove to be inaccurate as a result of factors beyond
its control, and actual results may differ materially from expected
results.

TSX Venture closing price for TRO-V
Date: 2017/09/21
Closing Price: 0.11

TEL:  (303) 716-5922  John J. Gardiner
CELL:  (720) 209-3049
EMAIL:  johnjgardiner@earthlink.net
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1726700017TS11726701408-06520720170925