Source	MARKET NEWS
Date	10/09/2018
Time	05:39:41 AM

Company	 Compass Gold Corporation
Title	Soil 
Geochemical Survey Identifies Numerous Gold





    CDNX Symbol: CVB











Press Release





COMPASS GOLD CORP ("CVB-V;COGDD-0")
- Soil Geochemical Survey Identifies Numerous Gold Anomalies
- Coincident With Crustal-Scale Faults on Kourou Permit

Compass Gold Corp. (Compass or the Company) is pleased to provide
an update on the now completed priority shallow soil geochemical survey
program over the Kourou and Tieloulena exploration permits on its
Sikasso Property in Southern Mali.

Highlights

*  Twelve discrete gold anomalies were identified on Kourou permit
along strike lengths up to 5 km
*  Highest soil sample contained 1.38 grams per tonne (g/t) gold
(Au)
*  Fourteen soil samples contained more than 0.1 g/t Au (100 ppb)
*  A total of 4,597 shallow soil samples were collected on the
Kourou and Tieloulena permits, where 689 shallow soil samples returned
above the 5 parts per billion (ppb) limit of detection
*  Mineralization is coincident with deep linear structures,
interpreted as faults, from a remote sensing study

Compass CEO, Larry Phillips, commented, "We are pleased to report
the results from our initial shallow soil program on Kourou, where we
have identified twelve linear anomalies over the length of the permit.
Most of the anomalies correspond with interpreted faults.  This
includes a 2-km anomaly associated with artisanal workings that
contained up to 5.04 g/t gold from grab samples.  Again, these initial
results give us confidence that we are following the right exploration
plan in an area that has been shown to contain several, rich gold
mines. Meanwhile, we are anxious to continue our work on these two
permits once the rains abate. At the same time, we will be initiating
the first bedrock drilling program on our Ouassada permit targets,
which are located approximately 50 km northwest of Kourou and
Tieloulena."

Kourou and Tieloulena

This latest program included 4,597 shallow soil samples collected
over the Kourou and Tieloulena permits (Figure 1).  Both permits lie to
the east of and within 45 km the Yanfolila Belt, a terrane boundary cut
by the Siekerole Shear Zone, which hosts several gold mines, including
Kalana (2.0 Moz Au), Kodieran (1.9 Moz Au) and Yanfolila (2.5 Moz Au).
Previous exploration on both permits has been minimal, and no drilling
has ever taken place.

Detailed Shallow Soil Results

The 4,597 shallow samples were collected from a depth of
approximately 0.4 m over 61% of the Kourou permit and 23% of the
Tieloulena permit on an east-west grid with a line spacing of 500 m and
a sample spacing of 100 m. The sample locations represent targets
identified by Compass geologists, and areas identified during a remote
sensing study by Murphy Geological Services (see Compass press release
dated May 28, 2018).

The figure above illustrates the location of the samples and their
anomalism in each permit.  As well as linear anomalies, there are
several discrete anomalies with single point samples, generally greater
than 100 ppb Au.  In Mali, soil samples greater than approximately 10
ppb Au are considered anomalous, and typically warrant further
investigation.  Linear anomalies are restricted to the Kourou permit,
where a total of 12 zones are identified (Figure 2).

A photo accompanying this announcement is available at
http://www.globenewswire.com/NewsRoom/AttachmentNg/c1d8d54e-a2d5-42cc-b597-
2848389f66a5

The anomalous zones vary in length from 1 to 5 km.  Generally, the
anomalies have north-northeast trends, but three anomalies have
northwest trends.  Some areas are defined by three-point anomalies,
which suggests zones up to 150 m wide.  The highest recorded gold
sample assayed beyond the limit of detection for the method (10,000 ppb
Au, or 10 g/t Au) and was located as an isolated anomaly at the extreme
south of the Kourou permit, south of the 2-km long anomaly 12.  The
second highest sample was 1.38 g/t Au, and it does not appear to be
closely related to any geological structures, and is not within a water
course.  The location of the anomalies generally corresponds to
interpreted deep crustal-scale faults.

Two anomalies are related to known gold workings.  Anomaly 1 (see
Figure 2) is located at Kosserefila, where a 200-m long and 100-m wide
zone of auriferous eluvial is currently being worked by artisanal
miners.  Grab samples by Compass geologists collected at this location
in 2017 returned gold assays of up to 5.04 g/t Au, and an independent
assay collected for the NI 43-101 report* contained 0.4 g/t Au, from a
depth of 0.4 m.  Shallow soil samples collected 100 m to the south of
the workings contained 12 ppb Au, and 500 m away, a sample with 141 ppb
was present.  One kilometre further south, along the same structure as
Kosserefila, a sample contained 886 ppb Au (or 0.886 g/t Au).  Anomaly
2 includes a 65 ppb Au shallow soil sample, and is present on a 1- km
long northeast-trending anomaly. This anomaly located 150 m to the
northeast of historic eluvial (soil) workings at Samagouela.

Anomaly 8, the longest one identified, is present over 5 km.
Anomalous gold grades defining the anomaly range from 26 to 76 ppb Au.
The anomaly appears to parallel a crustal-scale lineament (fault)
identified in the remote sensing study.  All of the anomalies appear to
be narrow, less than 200 m wide, and in-fill sampling will help to
better define their dimensions.

Several isolated gold soil anomalies containing gold greater than
100 ppb are present on the permits (Figure 1).  Additional sampling is
planned over these areas to determine the extent of mineralization.

Tieloulena Shallow Soil Sampling

A total of 1,197 shallow soil samples were collected on the
Tieloulena permit (Figure 1) on areas considered to be a priority based
on previous geological mapping generated by the MGS remote sensing
study.  Anomalism on the permit was much weaker than Kourou, which was
expected since the geology is dominated by sedimentary lithologies,
rather than the more prospective Birimian volcaniclastic rocks
occurring to the west.  The highest gold assay recorded was 205 ppb,
and was located in a stream bed, suggesting reworking and a subsequent
increase in gold grade.  No clearly defined linear anomalies were
identified on the permit.

Geology

Kourou and Tieloulena are underlain by Paleoproterozoic Birimian
volcanic, volcaniclastic, and sedimentary rocks, which have been
deformed and intruded by granitoids during orogenesis.  They lie to the
east of the Yanfolila Belt, a terrane boundary characterized by
deformation caused by the transpressional Siekerole Shear Zone, which
hosts several gold mines, including Kalana (2.0 Moz Au; Endeavour
Mining), Kodieran (1.9 Moz Au; Wassoul'Or S.A.) and Yanfolila (2.5 Moz
Au; Hummingbird Resources).

Next Steps

The results of the initial shallow soil sampling program on Kourou
are highly encouraging but require additional work to confirm the
continuity of gold anomalism between the sampling lines and between
samples.  The current spacing (500 m line spacing with samples
collected every 100 m) will be reduced to 100 m lines and samples
collected at 50 m intervals.  This will quickly identity areas that can
be investigated through the use of a deep soil auger sampling, with
penetration depths averaging 12 m.  This sampling will be a priority on
anomaly 1 due to the presence of near surface gold (5.04 g/t).

Regional shallow soil sampling will resume on both Kourou and
Tieloulena to fully test the gold potential of both permits.  The line
spacing for this grid will be 500 m, and a sample spacing of 100 m.
Both programs can be done relatively quickly after the current rainy
season, once weather and ground conditions are more favourable.

About Compass Gold Corp.

Compass, a public company having been incorporated into Ontario,
is a Tier 2 issuer on the TSX- V. Through the recent acquisition of MGE
and Malian subsidiaries, Compass holds gold exploration permits located
in Mali that comprise the Sikasso Property.   The exploration permits
are located in three sites in southern Mali with a combined land
holding of 1,179 km2. The Sikasso Property is located in the same
region as several other multi-million ounce gold projects, including
Morila, Syama, Kalana and Kodieran.  The Company's Mali-based technical
team, led in the field by Dr. Madani Diallo and under the supervision
of Dr. Sandy Archibald, P.Geo, is initiating a new exploration program.
They are examining the first of numerous anomalies noted for further
investigation in Dr. Archibald's August 2017 *"National Instrument
43-101 Technical Report on the Sikasso Property, Southern Mali."

QAQC

All samples were collected following industry best practices, and
an appropriate number and type of certified reference materials
(standards) and blanks were inserted to ensure an effective QAQC
program was carried out.  The samples were prepared at ALS Mali SARL
(Bamako, Mali) then transported to ALS Johannesburg (RSA) to be
analyzed by fire assay analysis.  All standard and blank results were
reviewed to ensure no failures were detected.

Qualified Person This news release has been reviewed and approved
by Dr. Sandy Archibald, P.Geo, Compass's Technical Director, who is the
Qualified Person for the technical information in this news release
under National Instrument 43-101 standards.

Forward-Looking Information This news release contains
"forward-looking information" within the meaning of applicable
securities laws, including statements regarding the Company's planned
exploration work and management appointments. Readers are cautioned not
to place undue reliance on forward-looking information. Actual results
and developments may differ materially from those contemplated by such
information. The statements in this news release are made as of the
date hereof. The Company undertakes no obligation to update
forward-looking information except as required by applicable law.



Contact:

//st

Compass Gold Corporation        Compass Gold Corporation

Larry Phillips - Pres. & CEO    Greg Taylor - Dir. Investor Relations &
Corporate Communications

lphillips@compassgoldcorp.com   gtaylor@compassgoldcorp.com

T: +1 416-596-0996 X 302        T: +1 416-596-0996 X 301

//et

Website: www.compassgoldcorp.com

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
RELEASE.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1828100002TS11828100778-05361520181009