Source	MARKET NEWS
Date	10/01/2018
Time	05:51:01 AM

Company	 Belmont Resources Inc.
Title	Additional Assays From Drilling At Kibby Basin,





    CDNX Symbol: BEA











Press Release





Additional Assays From Drilling At Kibby Basin, Nevada LithiumProject; Up To 
580ppm Lithium --->@NEWS RELEASE
MGX MINERALS INC ("XMG-Z;MGXMF-0")
BELMONT RESOURCES INC ("BEA-V")
- Additional Assays From Drilling At Kibby Basin, Nevada Lithium
- Project; Up To 580ppm Lithium

MGX Minerals Inc. ("MGX" or the "Company") announces that
joint-venture partner Belmont Resources ("Belmont") has released
additional assay results from 25 core samples collected in drill hole
KB-3 (1,270 - 1,798 feet) at the Kibby Basin lithium project ("Kibby
Basin"). As reported by Belmont, 20 of 25 samples exceeded greater than
100 ppm lithium, with seven samples containing greater than 300ppm
lithium, and the highest sample containing 580ppm lithium.

Lithium at Kibby Basin is enriched in clay-rich samples. Ash
layers accounted for four of the five low lithium samples, suggesting
that initial lithium content may have been leached from the porous ash
layers and transported to brines elsewhere in the basin. The boreholes
targeting the southern portion of a large MT conductor still offer
potential to identify saturated sediments containing lithium-rich
brines.

//st

Table 1. Kibby KB-3C Assay Results

Feet                                 Recovered Weight(ppm)   Lithium (ppm)

1278-1281                            1.09                    207

1316-1318                            1.27                    140

1344-1348                            1.88                    181

1384-1388                            2.54                    263

1403-1406                            1.78                    386

1411-1412                            0.37                    51.9

1412-1412.3                          0.08                    13

1413-1414.5                          0.96                    226

1434-1438                            2.9                     418

1441.8-1445                          0.2                     33.7

1452-1454.5                          2.33                    375

1480-1490                            0.88                    9.5

1490.5-1492.5                        1.44                    408

1528-1532                            1.15                    395

1538-1542                            2.1                     212

1596-1598                            1.2                     375

1598-1598.5                          0.26                    24.1

1726-1730                            2.13                    274

1730-1731.5                          0.36                    292

1746-1750                            2.75                    240

1768-1771.5                          2.35                    417

1791-1791.5                          0.28                    580
1793-1798                            2.43                    290

1440-1442                            1.5                     -

1485.5-1488                          1.1                     -

//et

25 samples of representative core were selected for assay from
this lower part of drilling and were delivered to ALS Labs in Reno,
Nevada on August 31, 2018 for 41-element ICP analysis (including Li).

Samples were of ash layers, silicified sediments, and high pyrite
and magnetite zones. Based on Quantec MT geophysics, the proposed
second hole (KB-4, AKA 2018-2) would likely mimic hole 3 with redox
boundary (and aquifer) at 900 -1000 ft. depth, and reduced clays with
high Li content below 1,000 ft.

The Kibby Basin shares many characteristics with Clayton Valley,
where lithium brines are being exploited, including: closed structural
basin, large conductor at depth, lithium anomalies at surface and
depth, evidence of a geothermal system, and potential aquifers in
porous ash and gravel zones.

About the Kibby Basin Lithium Brine Partnership

MGX is partnered with Belmont Resources on the Property and
currently earning a 50% interest with the goal of forming a 50/50 Joint
Venture (the "Joint Venture") to utilize MGX's rapid lithium extraction
technology. Kibby Basin is located in the western portion of the Great
Basin in Nevada. The property covers 2,560 acres located in Esmeralda
County, Nevada. Geologic research of the Kibby Basin has indicated that
proximal rhyolitic flows and tuffs surrounding the basin could be a
potential source of Li brine in the Kibby Basis Playa. In addition, the
Kibby Basin is located within a geothermal cluster at a basin low
setting. Regional geophysical signatures in the area reflect similar
anomalies comparative to that of Clayton Valley, approximately 50km to
the South, location of Abermarle's Silver Peak Mine, the only North
American lithium producer.

Rapid Lithium Brine Extraction Technology

MGX has developed a rapid lithium extraction technology
eliminating or greatly reducing the physical footprint and investment
in large, multi-phase, lake sized, lined evaporation ponds, as well as
enhancing the quality of extraction and recovery across a complex range
of brines as compared with traditional solar evaporation. This
technology is applicable to petrolithium (oil and gas wastewater),
natural brine, and other brine sources such as lithium-rich mine and
industrial plant wastewater. The technology was recently chosen as
winner of the Base and Specialty Metals Industry Leadership Award at
the 2018 S&P Global Platts Global Metals Awards, held in London in May
(see press release dated May 18, 2018).

Qualified Person

Andris Kikauka (P. Geo.), Vice President of Exploration for MGX
Minerals, has prepared, reviewed and approved the scientific and
technical information in this press release. Mr. Kikauka is a
non-independent Qualified Person within the meaning of National
Instrument 43-101 Standards.

About MGX Minerals

MGX Minerals is a diversified Canadian resource company with
interests in advanced material and energy assets throughout North
America. Learn more at www.mgxminerals.com.

Neither the Canadian Securities Exchange nor its Regulation
Services Provider (as that term is defined in the policies of the
Canadian Securities Exchange) accepts responsibility for the adequacy
or accuracy of this release.

Forward-Looking Statements

This press release contains forward-looking information or
forward-looking statements (collectively "forward-looking information")
within the meaning of applicable securities laws. Forward-looking
information is typically identified by words such as: "believe",
"expect", "anticipate", "intend", "estimate", "potentially" and similar
expressions, or are those, which, by their nature, refer to future
events. The Company cautions investors that any forward-looking
information provided by the Company is not a guarantee of future
results or performance, and that actual results may differ materially
from those in forward-looking information as a result of various
factors. The reader is referred to the Company's public filings for a
more complete discussion of such risk factors and their potential
effects which may be accessed through the Company's profile on SEDAR at
www.sedar.com.

TEL:  1.604.681.7735  Jared Lazerson, President and CEO
WEBSITE:  www.mgxminerals.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1827300010TS11827301073-05455220181001