Source	MARKET NEWS
Date	10/01/2018
Time	06:29:43 AM

Company	 Millrock Resources Inc.
Title	Millrock 
Partner Reports Drill Intersections





    CDNX Symbol: MRO











Press Release





MILLROCK RESOURCES INC ("MRO-V")
- Millrock Partner Reports Drill Intersections

Millrock Resources Inc. ("Millrock") announces that PolarX Mining
Inc. ("PolarX") (ASX: PXX) has reported additional assay results for
2018 from drilling at the Zackly copper-gold deposit within its Alaska
Range Project.

The following two drill intersections are from hole ZX-18020 and
ZX-18024:

//st

Hole ID            From      To (m)   Interval      Cu%    Au g/t   Ag
g/t
(m)                (m)

ZX-18020           2.5       57.1     54.6          0.6*   2.8      9.5

Including:         2.5       14.0     11.5          0.6    5.3      12.0

and:               18.3      27.1     8.8           0.5    5.8      4.5

and:               32.0      43.3     11.3          0.8    1.8      23.3

and:               46.2      57.1     10.9          1.0*   1.6      3.9

ZX-18024           37.0      83.7     46.7          0.6    3.1      3.3

Including:         59.0      80.7     21.7          0.8    5.2      4.1

These intersections include an uncut assay grading 27.3% Cu over a narrow
interval of 0.3 meters between 56.7 meters and 57.0 meters.

//et

Both holes were drilled on the same section 850 meters east of the
Zackly copper-gold-silver skarn deposit. ZX-18024 was drilled to
undercut hole ZX-18020 by approximately 40 meters. The mineralization
begins just below surface and appears to be gently dipping at around 20
degrees. If the interpretation is correct the drilled intersections are
close to true width. The mineralization is hosted in skarn displaying
relict bedding and occurs in quartz-sericite veining and is open along
strike and down dip. Further details with a map and cross section can
be found in the September 25, 2018 announcement made by PolarX, which
is available on their website.

The next two drill intersections are from hole ZX-18023 and
ZX-18025:

//st

Hole ID    From (m)   To (m)   Interval (m)   Cu%   Au g/t   Ag g/t

ZX-18023   20.8       30.1     9.3            3.3   2.3      19.7

ZX-18025   84.8       99.8     15.0           2.3   2.2      11.9

//et

Both holes were drilled on the same section, 350 meters east of
the Zackly copper-gold-silver skarn deposit. ZX-18025 was drilled too
intersect approximately 40 meters beneath the mineralization
intersected in hole ZX-18023, which confirmed the intersection of
historic hole Z86. The intersections indicate steeply dipping,
high-grade copper-gold mineralization like that observed in the Zackly
deposit. The mineralization is of the magnetite skarn variety with
copper sulfides occurring as disseminated and vein-hosted chalcopyrite
and bornite. Given the near-vertical orientation of the mineralized
zone, the true width is interpreted to be about 65% to 70% of the drill
interval indicated in the table above. Further details with a map and
cross section can be found in the September 20, 2018 announcement made
by PolarX, which is available on their website.

Exploration at the Alaska Range Project is being done by Millrock
on behalf of PolarX. Millrock presently owns 6.44% of the issued and
outstanding PolarX shares and is entitled to certain milestone and
royalty payments on portions of the project.

Quality Control - Quality Assurance Millrock adheres to stringent
Quality Assurance - Quality Control (QA/QC) standards. Drill core
samples are kept in a secure location at all times. Representative half
core samples were collected and assayed at ALS Chemex laboratories in
Vancouver, Canada and Reno, Nevada, USA, after being prepared at the
preparatory laboratory in Fairbanks, Alaska, USA. Gold was analyzed by
Fire Assay (specifically ALS code Au-AA25 - Au by fire assay and AAS
using a 30 gram nominal sample weight). Other elements (33 in total
including copper) were analyzed using ALS method code ME-ICP61 which
involves a four-acid digest and an ICP-MS finish. Over range (Cu )= 1%)
was analyzed using ALS method code ME-OG62 which involves a four-acid
digest and an ICP-AES or AAS finish. The following QA/QC protocols have
been adopted for this program: 1) Blank samples and Standards -
Certified Reference Material (CRM's) account for approximately 10% of
core samples submitted to the laboratory, 2) QA/QC samples are spaced
no more than ten samples apart, 3) geologists instruct the lab to run
clean rock through equipment immediately following samples containing
visible native gold and / or copper, and 4) the laboratory prepares
coarse crush and fine pulverized duplicate samples and analyzes the
duplicates. All results from blanks, standards and duplicates were
reviewed and found to be accurate within acceptable tolerances for
results obtained to date. The Qualified Person is of the opinion that
the results reported in this press release are reliable.

Qualified Person The scientific and technical information
disclosed within this document has been prepared, reviewed and approved
by Gregory A. Beischer, President, CEO and a director of Millrock
Resources. Mr. Beischer is a Qualified Person as defined in NI 43-101.

About Millrock Resources Inc. Millrock Resources Inc. is a premier
project generator to the mining industry. Millrock identifies, packages
and operates large-scale projects for joint venture, thereby exposing
its shareholders to the benefits of mineral discovery without the usual
financial risk taken on by most exploration companies. The company is
active in Alaska, British Columbia, the southwest USA and Sonora State,
Mexico. Funding for drilling at Millrock's exploration projects is
primarily provided by its joint venture partners. Business partners of
Millrock have included some of the leading names in the mining
industry: Centerra Gold, First Quantum, Teck, Kinross, Vale, Inmet,
Altius, and Riverside. Millrock is a major shareholder of junior
explorers PolarX Ltd. and Sojourn Exploration Inc.

ON BEHALF OF THE BOARD
Gregory Beischer, President & CEO

Melanee Henderson, Investor Relations
(604) 638-3164
(877) 217-8978 (toll-free)

Some statements in this news release contain forward-looking
information. These statements address future events and conditions and,
as such, involve known and unknown risks, uncertainties and other
factors which may cause the actual results, performance or achievements
to be materially different from any future results, performance or
achievements expressed or implied by the statements. Such factors
include without limitation the completion of planned expenditures, the
ability to complete exploration programs on schedule and the success of
exploration programs.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1827300030TS11827301488-06260520181001