Source	MARKET NEWS
Date	09/25/2018
Time	06:14:15 AM

Company	 Aben Resources Ltd.
Title	Intersects 
Additional, Shallow High Grade Gold M





    CDNX Symbol: ABN











Press Release





ABEN RESOURCES LTD ("ABN-V;ABNAF-0")
- Intersects Additional, Shallow High-Grade Gold Mineralization
- at the North Boundary Zone of the Forrest Kerr Project in BC's
- Golden Triangle

Aben Resources Ltd. (the "Company") announces that additional
analytical results have been received from the early-stage drilling at
the 23,000 hectare Forrest Kerr Property (the "Property") located in
the Golden Triangle region of British Columbia. The eight drill holes
reported here consist of step-out drilling at the North Boundary Zone
and most of the holes intersected shallow, high-grade gold
mineralization. Highlights include: 5.08 g/t Au over 12.0m in hole
FK18-12; 23.3 g/t Au over 2.0m in hole FK18-13; and 10.62 g/t Au over
3.0m in hole FK18-17. To date, final analytical results have been
received for 3,000m of a total projected 10,000m (table of values and
hole descriptions near end of release).

Golden Triangle, B.C., claims map:
https://www.abenresources.com/site/assets/files/4287/fk-003.jpg

This step-out drilling has successfully expanded the North
Boundary Zone along an interpreted NE-SW trend from the high-grade gold
mineralization reported last year in holes FK17-04, 05, and 06 as well
as in previously reported FK18-10 which intersected 38.7 g/t Au over
10.0m from 114.0m - 124.0m depth including 62.4 g/t Au over 6.0m (see
news release dated August 9, 2018). Several discrete zones of
Au-Ag-Cu-Zn mineralization were encountered in all eight drill holes
reported here and the multiple mineralized horizons illustrate the
strong potential for further discovery of precious metal bearing
structures on the Property.

Highlights:

*  Hole FK18-12 returned 5.08 g/t Au over 12.0m (40.0m - 52.0m
depth), including 24.25 g/t Au over 2.0m (42.0m - 44.0m depth)
*  Hole FK18-13 returned 23.3 g/t Au over 2.0m (106.0m - 108.0m
depth)
*  Hole FK18-17 returned 3.18 g/t Au over 15.0m (232.0m - 247.0m
depth) including 11.02 g/t Au over 2.0m (239.0m - 241.0m depth), as
well as 31.40 g/t Au over 1.0m (261.0m - 262.0m depth)
*  North Boundary Zone remains open in all directions
*  36 drill holes completed to date with assays pending for 27 of
these holes which were drilled using Oriented Core Drilling techniques
*  Drilling continues as part of an expanded program
*  Broad soil geochemical anomaly over 4 km in length and
continues to yield new discoveries (i.e.: recently-announced South
Boundary Zone where final assays are still pending)
*  New airborne geophysical survey reveals numerous untested
target areas

Jim Pettit, President and CEO of Aben Resources stated, "These
high-grade step-out holes at North Boundary have expanded the zone
which is open in all directions and confirm the presence of a robust
mineralizing system in the area. Based on the geochemical and new
geophysical data available to us we can clearly see the potential of
the area that now includes the North Boundary Zone, the historic
Noranda hole 230 meters to the south and the South Boundary Zone
another 1.5 kilometers further south. Given the complex geology, we
started using Oriented Drill Core techniques after these eight holes
reported here which will help in identification of orientation and
structure as well as to delineate additional high-grade mineralization.
The target areas in and around the Boundary Zones are relatively
shallow and continue to provide strong discovery potential as we have
only systemically tested a very small area at shallow depths. The
Company is awaiting additional assay results from 27 holes, three of
which are from South Boundary and the rest from the North Boundary
Zone. This new high-grade discovery is still in its early days and with
this increased drill program there will be news for some time to come.
I would also like to welcome Eric Sprott as a new major shareholder
and thank him for his support.  The Company now has just over $7
million in the treasury from financings and the exercise of warrants. "


Complete assays for the three holes collared 1.5 km south at the
South Boundary Zone are still pending. The South Boundary Zone had
never been drill-tested and the newly discovered mineralization is
encouraging considering the distance between the collar locations in
the North and South Boundary Zone. The ground between and beyond the
two zones is highly prospective for further discovery of gold and
copper-bearing horizons given that they are located within a large
gold-in-soil and rock anomaly in similar lithologies. The ubiquitous
nature of the veining and widespread alteration regimes indicates that
a strong and extensive hydrothermal system operated throughout time
across the Boundary Zone. The broader soil geochemical anomaly that
covers both the North and South Boundary Zones extends for over 4 km
north to south and 1.5 km east to west.

Boundary Area Soil Geochemical map:
https://abenresources.com/site/assets/files/4855/abn_new_boundary_map.jpg


Aben has also just completed a 355 line-kilometer airborne
Magnetic survey over the entire Boundary Zone with results expected by
the end of September. The interpreted results of the survey are
expected to greatly assist in identifying fault structures that have
good potential to host high-grade precious metal mineralization in the
Boundary valley. Mineralization at Boundary is structurally controlled
and hosted in a package of volcanic and volcaniclastic rocks from the
Jurassic Hazelton Group. Several generations of quartz and
quartz-carbonate veining are important hosts to mineralization, as are
subordinate breccia zones with strong chlorite, hematite and carbonate
alteration. The Boundary Zones lie between the Forrest Kerr Fault to
the west, a major deep-seated crustal feature, and the unconformable
contact between the Jurassic Hazelton Group and the Triassic Stuhini
Group to the East. The rock reflects a prolonged history of strong
hydrothermal activity combined with brittle deformation. The Boundary
host package Hazelton rocks are also known to be a prolific host to
several deposits throughout the region. The North Boundary area shows
very little outcrop exposure and contains complex geology which is
disrupted by a series of faults of unknown orientation. All additional
drilling is implementing Oriented Core Drilling techniques which will
aid in determining true thicknesses and establishing structural and
lithologic controls to mineralization.

Table of Assay Results:

//st
Hole ID                        From     To (m)   Interval    Au      Cu
(m)               (m)         (g/t)   (ppm)

FK18-11                        334.0    337.0    3.0         2.09    923

incl           336.0    337.0    1.0         4.55    17

FK18-12                        40.0     52.0     12.0        5.08    1993

incl           40.0     46.0     6.0         8.78    3965

incl           41.0     45.0     4.0         13.03   5907

incl           42.0     44.0     2.0         24.25   11575

FK18-13                        106.0    108.0    2.0         23.30   350

FK18-14         no
significant
results

FK18-15         hole lost
at 61.5m

FK18-16                        303.0    307.0    4.0         3.13    2219

incl           303.0    304.0    1.0         6.95

FK18-17                        232.0    247.0    15.0        3.18    598

incl           238.0    243.0    5.0         5.60    570

incl           239.0    241.0    2.0         11.02   169

260.0    263.0    3.0         10.62   7562

incl           261.0    262.0    1.0         31.40   19750

283.0    284.0    1.0         8.22    9110

FK18-18                        233.0    237.0    4.0         4.02    2317

incl           234.0    236.0    2.0         6.99    3985
*all assay values are uncut and intervals reflect drilled
intercepts true thicknesses and orientations of the various zones
is currently not known

//et

North Boundary Plan View Drill map:
https://www.abenresources.com/site/assets/files/4299/abn_north_boundary_pla
n_2_map_sept__2018.jpg

Summary of Drilling:

FK18-11: same pad as FK18-10 at a steeper angle Several intercepts
) 1.0 g/t Au were encountered (high 4.55 g/t) throughout its 402m
length

FK18-12: collar location 40 meters NE of FK18-10 & 11 Collared in
mineralization at 12.0m (3.5 g/t Au) with a shallow zone between 40-52m
that returned 5.1 g/t Au over 1.0m including 34.3 g/t Au over 1.0m

FK18-13: collar location same as above Mineralization at or near
top returned between 1-3 g/t Au with a high of 23.3 g/t Au over 1.0m at
106m depth

FK18-14 & 15: collar location 50m SW of FK18-10 & 11 Both holes
encountered broken and faulted ground conditions that were poorly
mineralized and in the case of FK18-15 lost at 61m

FK18-16: collar location as above at steeper dip (-65) Narrow
zones of low grade ((1 g/t) gold mineralization near top with a strong
sulfide horizon at 300m that returned 1.7 g/t Au over 8.0m

FK18-17 & 18: collar location 185m SW of FK18-10 and drilled
opposite direction (northward) FK18-17 (-45) pierced a 15.0m zone that
tested 3.2 g/t Au with an intercept of 31.4 g/t Au 20m below this zone
(240m depth) FK18-18 (-50) hit the same zone of above with 4.0 g/t Au
over 4m.

Link to additional Cross Section and Plan View maps:
https://www.abenresources.com/projects/photo-gallery/

Analytical and QA/QC Description:

All 1- or 2-meter drill core samples were delivered to ALS Global
prep facility in Terrace, British Columbia where they were crushed
until 70% passed a 2mm sieve, then a 250g split was pulverized until
better than 85% passed a 75-micron screen. Gold was tested via fire
assay method Au-ICP21 with all ore-grade samples ()10 g/t) undergoing
fire assay with gravimetric finish. ALS performed multi-element ICP-AES
package ME-ICP41 in their Vancouver facility to test for 35 other
elements. In addition to the quality assurance and quality control
program performed by ALS, Aben personnel insert lab certified
standards, field blanks and duplicates into the sample stream at the
rate of one QA/QC sample in every 10 samples.

Cornell McDowell, P.Geo., V.P. of Exploration of Aben Resources,
has reviewed and approved the technical aspects of this news release
and is the Qualified Person as defined by National Instrument 43-101.

About Aben Resources:

Aben Resources is a Canadian gold exploration company developing
projects in British Columbia's Golden Triangle, the Yukon, and
Saskatchewan. The Company is actively exploring its flagship and
high-grade Forrest Kerr Project located in the Golden Triangle region
where recent drilling has discovered strong precious and base metal
mineralization at the North Boundary Zone.

For further information on Aben Resources Ltd. (TSX-V: ABN), visit
our Company's web site at www.abenresources.com.

ABEN RESOURCES LTD.

"Jim Pettit"

JAMES G. PETTIT
President & CEO

For further information contact myself or: Don Myers Aben
Resources Ltd. Director, Corporate Communications Telephone:
604-687-3376 Toll Free: 800-567-8181 Facsimile: 604-687-3119 Email:
info@abenresources.com

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

This release includes certain statements that may be deemed to be
"forward-looking statements". All statements in this release, other
than statements of historical facts, that address events or
developments that management of the Company expects, are
forward-looking statements. Although management believes the
expectations expressed in such forward-looking statements are based on
reasonable assumptions, such statements are not guarantees of future
performance, and actual results or developments may differ materially
from those in the forward-looking statements. The Company undertakes no
obligation to update these forward-looking statements if management's
beliefs, estimates or opinions, or other factors, should change.
Factors that could cause actual results to differ materially from those
in forward-looking statements, include market prices, exploration and
development successes, continued availability of capital and financing,
and general economic, market or business conditions. Please see the
public filings of the Company at www.sedar.com for further information.

TEL: 604-687-3376    ABEN RESOURCES LTD
FAX: 604-687-3119
E-mail: info@abenresources.com
Website: http://www.abenresources.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1826700021TS11826701231-06100420180925