Source	MARKET NEWS
Date	09/18/2018
Time	05:26:01 AM

Company	 Ashanti Gold Corp.
Title	Additional 
Results for Gourbassi West, Kossanto





    CDNX Symbol: AGZ











Press Release





ASHANTI GOLD CORP ("AGZ-V;GULSF-0")
- Additional Results for Gourbassi West, Kossanto
- East Project, Mali

Ashanti Gold Corp. ("Ashanti" or the "Company") announces
additional new results from Gourbassi West.  These most recent drill
hole results were part of a recently completed 105 hole Reverse
Circulation ("RC") and Diamond Drill ("DD"), 12,283 metre drill program
that tested mineralization on the Kossanto East Project (the
"Property") in western Mali (Figure 1). Results presented here are from
section 1485800 (Figures 2 and 3), south of sections previously
described in the Company's August 14 and August 27 press releases.  The
mineralized zones in these sections demonstrate strike continuity of
mineralization and coherence of interpreted thrust faults and their
relationship to mineralization.  These results also support and expand
on previously interpreted mineralized zones dipping moderately to the
west. Importantly, as we develop our understanding of the
mineralization, it is becoming increasingly apparent that there are
numerous zones of mineralization associated with stacked thrust faults.
In this section alone, the combined width of mineralized zones is
approximately 130m.  If mineralized zones to the north continue to this
section, there is potential for an additional 100m of mineralized
width.
Tim McCutcheon, CEO, said, "These results continue to build upon
the overall strike line of Gourbassi West. We are getting closer to
completing our resource calculations, and it is exciting to see how the
cross sections fall into place with our geological modelling and
understanding of the Property."

Gourbassi West Gourbassi West is the second of two principle areas
of mineralization being investigated by the company at Kossanto East.
The target consists of gold mineralization associated with silicified,
brecciated felsic volcanic rocks along a northwest trending structural
zone for over 1,200m of strike length.  2018 diamond drilling revealed
that the silicified brecciated volcanic rocks that host most of the
gold mineralization are associated with shallow to moderately west
dipping thrust faults.  Sedimentary rocks that are younger than the
host volcanic rocks and occur to the east of mineralization (Figure 2)
are in fault contact with, and are overlain by older volcanic rocks.
This is a classic 'older over younger' thrust fault structural
relation.  Repetition of this pattern reveals that mineralization is
associated with cross-cutting and stacked thrust surfaces.

//st

Section   Hole      From     To      Interval*    Grade    Comments
(m)      (m)     (m)          (g/t)

1485800   GWRC271   0        2       2            0.27

5        7       2            0.59

22       53      31           0.81

incl.     30       38      8            1.32

56       57      1            0.55

74       76      2            0.31

77       79      2            0.20

GWRC272   4        6       2            0.40

9        10      1            0.20

59       61      2            0.29

70       80      10           1.03

incl.     75       79      4            1.86

81       82      1            0.34

89       90      1            0.22

90       93      3            0.49

95       100     5            0.63

103      107     4            0.45

109      111     2            0.45

114      120     6            0.30

122      126     4            0.50

134      135     1            0.23     hole ends in
mineralization

GWRC273   13       33      20           0.60

38       39      1            5.31

41       42      1            0.22

45       55      10           0.59

incl.     47       48      1            2.58

65       66      1            0.32

68       69      1            0.25

69       78      9            0.40

97       98      1            0.39

101      103     2            0.31

110      111     1            0.28

122      125     3            0.44     hole ends in
mineralization

//et

*Intervals indicated are not true widths as there is insufficient
geologic information to calculate true widths. However, drill holes
have been drilled to cross interpreted mineralized zones as close to
perpendicular as possible.

Figure 1 is available at
http://www.globenewswire.com/NewsRoom/AttachmentNg/5e3046e0-52df-439a-9fb3-
b4d9d75e7703

Figure 2 is available at
http://www.globenewswire.com/NewsRoom/AttachmentNg/32f90703-16c7-4e25-bbb0-
04311c46c77c

Figure 3 is available at
http://www.globenewswire.com/NewsRoom/AttachmentNg/8ef96ab8-c64a-40f2-9e2b-
d8223a29f066

About Kossanto East Project The Kossanto East Project is a 66.41
km2 concession in the prolific Kedougou - Kenieba Inlier, the
northwestern most exposure of Birimian rocks in West Africa and host to
the Loulo and Sadiola group of world class gold deposits.  The Property
hosts two principle historically drill-tested targets, Gourbassi East
and Gourbassi West and several surface anomalies identified in historic
surface samples and Rotary Airblast (RAB) drill holes. Geochemical
anomalies identified by previous explorers led to drill testing and
successful intersection of gold mineralization. The results reported
here are from Gourbassi West. Further results from Gourbassi West are
anticipated in the coming weeks.

ABOUT ASHANTI GOLD Ashanti is a gold-focused, exploration and
development company that targets projects where it has a competitive
advantage due to past work experience of the team and specific project
know-how. The Company is driving forward its 100%-owned Kossanto East
project in Mali on the prolific Kenieba Belt, which hosts such deposits
as Loulo, Fekola and Sadiola. Ashanti is also working to advance,
together with its earn-in partners, the Anumso project and the Ashanti
Belt project in Ghana, which are near-adjacent to the Akyem deposit.

On Behalf of the Board of Directors of ASHANTI GOLD CORP.

"Tim McCutcheon"

Tim McCutcheon CEO

Contact Information:

Contact:
Ashanti Gold Corp.
2300 - 1177 West Hastings Street
Vancouver BC, V6E 2K3
Phone: 604-638-3847

Qualified Person and Quality Assurance / Quality Control

Dr. Paul Klipfel, CPG (AIPG certification #10821), Ashanti's COO
and Chief Geologist is a Qualified Person as defined by Canadian NI
43-101 and has supervised the preparation of the scientific and
technical information that forms the basis for this news release. Dr.
Klipfel is responsible for all aspects of the work including the
Quality Control/Quality Assurance programs. Dr. Klipfel is not an
Independent Person, as he is a shareholder of Ashanti.
Certified Reference Materials and Blanks are inserted into the
sample stream at the rate of 1:20 samples.  Field duplicates are
collected at the rate of 1:50 samples.  All samples have been analyzed
by SGS Laboratories in Bamako with standard preparation methods and 50g
fire assay with atomic absorption finish.  SGS does their own
introduction of QA/QC samples into the sample stream and reports them
to Ashanti for double checking.  Higher grade samples are reanalyzed
from pulp or reject material or both.

Cautionary Statement on Forward-Looking Information

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
RELEASE.

This press release contains forward-looking statements and
forward-looking information (collectively, "forward looking
statements") within the meaning of applicable Canadian securities
legislation. All statements, other than statements of historical fact,
included herein including, without limitation, statements regarding the
anticipated content, commencement, timing and cost of exploration
programs, anticipated exploration program results, the discovery and
delineation of mineral deposits/resources/reserves, and the anticipated
business plans and timing of future activities of the Company, are
forward-looking statements. Although the Company believes that such
statements are reasonable, it can give no assurance that such
expectations will prove to be correct. Forward-looking statements are
typically identified by words such as: believe, expect, anticipate,
intend, estimate, postulate and similar expressions, or are those,
which, by their nature, refer to future events. The Company cautions
investors that any forward-looking statements by the Company are not
guarantees of future results or performance, and that actual results
may differ materially from those in forward looking statements as a
result of various factors, including, but not limited to, the state of
the financial markets for the Company's equity securities, the state of
the commodity markets generally, variations in the nature, quality and
quantity of any mineral deposits that may be located, variations in the
market price of any mineral products the Company may produce or plan to
produce, the inability of the Company to obtain any necessary permits,
consents or authorizations required, including TSXV acceptance, for its
planned activities, the inability of the Company to produce minerals
from its properties successfully or profitably, to continue its
projected growth, to raise the necessary capital or to be fully able to
implement its business strategies, and other risks and uncertainties
disclosed in the Company's latest interim Management Discussion and
Analysis and filed with certain securities commissions in Canada. All
of the Company's Canadian public disclosure filings may be accessed via
www.sedar.com and readers are urged to review these materials,
including the technical reports filed with respect to the Company's
mineral properties.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1826000004TS11826000618-05231920180918