Source	MARKET NEWS
Date	10/09/2018
Time	09:03:55 AM

Company	 Dios Exploration Inc.
Title	Updates 
Fieldwork on Three Gold Properties in th





    CDNX Symbol: DOS











Press Release





DIOS EXPLORATION INC ("DOS-V;DIOSF-0")
- Updates Fieldwork on Three Gold Properties in the Lower
- Eastmain Deformation Zone, James Bay, Quebec

DIOS EXPLORATION completed exploration campaigns on three
wholly-owned gold projects in prospective Quebec Lower Eastmain
Deformation Zone, James Bay Eeyou Istchee, which are AU33, CLARKIE and
K2.

Advices were forwarded to DIOS last week from Val d'Or Assay
Office confirming receipt of 366 rock samples taken recently on these 3
properties.  Rock sample processing is being undertaken.  DIOS is
expecting the gold results in the short term (maybe a little longer for
base metals) and took 183 B-horizon soil samples when not outcropping.

First on AU33, prospecting targeted strategic parts of this large
property.  CLN gold discovery extents (Chain Lake North) were explored
and sampled in strike extent of 3.26 grams per tonne gold over 6 m true
width in a wider interval of some 2 g/t gold over 11 m.  Chain Lake
South and Chain Lake West (1 km west) were prospected and sampled
(rocks and soils) as well as the ROBINO (37 g/t gold) induced
polarization anomaly, which was soil sampled to define drill targets.
Adjoining eastwest Chain Lake break had returned very strong anomalous
gold-in-soil anomalies in that area along a 1.75 km strike also giving
high potential to this whole area 4 km north of HEBERTO GOLD.

A several sq. kilometer area that is not outcropping some 8 km
east of HEBERTO gold showing was soil sampled.  There were two magnetic
horizons in the fold nose.  The most eastern one showed induced
polarization (IP) anomalies and some were drill tested with some short
holes.  Some foliated tonalite dykes returned up to 1.56 g/t gold /1 m
& 1.02 g/t gold / 2 m. The western magnetic tonalite horizon is bush
covered, has no IP anomalies and was not yet tested: a B-horizon soil
survey was completed on that horizon in its nose and northern flank to
define drill targets.  This specific marker horizon was previously
mapped upice (highest assay: 0.8 g/t gold) in the fold northern flank.

So a group of unexplained high gold-in-till anomalies (0.576;
0.619; 0.731;  0.777;  1.255;  1.390;   2.090 g/t gold in heavy mineral
concentrates) is located upice of HEBERTO GOLD, a local source is
suspected, but the area is covered by till drumlins and poorly
outcropping.

Secondly, on the other hand, DIOS pursued exploration still
further upice of these gold-in-till anomalies: some 25 km north-east in
the ice flow direction was discovered by DIOS the Wacky gold showing
(8.8 g/t gold and 6.8 g/t gold) on CLARKIE.  See Sept. 19 press
release.  Recent lateral prospecting uncovered a pyritized sedimentary
unit very strongly altered in silica and sericite over at the very
least 3 km in strike and 20-25 m large, with a sub-vertical dip, so the
surface outcrops represent a rather true width.  After much prospecting
in the CLARKIE sedimentary basin, this is the first time DIOS hits such
pyrite, silica and sericite contents and alterations.  THESE ARE NOT
QUARTZ VEINS, but rather pervasive silica alteration.  Some 195 rock
samples (incl.19 quality control samples) and 64 B-horizon soils were
taken and the rock surface can often be reached with a shovel when
digging for soil samples.

Thirdly, several tens of km more to the west of AU33, still along
the Lower Eastmain Deformation Zone, the K2 property was prospected and
sampled, particularly on its new promising Far West claims and the WI
(west inputs) target, that had returned 6.72 g/t gold in a very large
sub-in place dacitic boulder and up 0.222 g/t gold in soils.

DIOS' team is very enthusiastic about rocks and alteration
identified and is awaiting results with expectancy.  DIOS' AU33 gold
property is road accessible 50 km south of Eleonore world-class gold
mine and 15 km west of Clearwater gold deposit.  This release was
prepared by MJ Girard, M.Sc. Geo 43-101 QP.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TEL:  (514) 923-9123      Marie-Jose Girard, President & CEO
E-mail: mjgirard@diosexplo.com
WWW.DIOSEXPLO.COM
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1828100037TS11828102276-09025720181009