Source	MARKET NEWS
Date	10/09/2018
Time	09:18:55 AM

Company	 Plateau Energy Metals Inc.
Title	Plateau Confirms Western Extension





    CDNX Symbol: PLU











Press Release





Plateau Confirms Western Extension --->@NEWS RELEASE
PLATEAU ENERGY METALS INC  ("PLU-V;PLUUF-0")
- Plateau Confirms Western Extension

Plateau Energy Metals Inc. ("Plateau" "PLU" or the "Company") is
pleased to announce the first drill results from Falchani West
drilling.

Falchani West Highlights

Figure 1 Falchani Project East-West Cross Section & Location Map
T13

Figure 2 Falchani Project East -West Cross Section  & Location Map
T14

*  65 m of 3,374 ppm Li (0.73% Li(sub)2(/sub)O) from 9-74 m in
Li-rich tuff unit within broader interval of 172 m of 2,908 ppm Li
(0.63% Li(sub)2(/sub)O) from 7-179 m (End of Hole - EOH) (PLAT14-V
Vertical Hole)

*  93 m of 2,839 ppm Li (0.61% Li(sub)2(/sub)O) from 42-135 m in
lithium tuff unit, within 104 m of 2,728 ppm Li (0.59% Li(sub)2(/sub)O)
from 39 to 143 m (EOH) in lithium tuff and upper and lower breccia
units (PLAT13-V Vertical Hole)

*  Both drill holes terminated in lithium bearing lower breccia
unit, which remain open at depth

*  Falchani West target area is a relatively new zone identified
through ground mapping and sampling where highly anomalous lithium
values now cover a footprint of )1.5 km E-W by approximately 1.7km N-S

*  Three rigs are currently active at Falchani West with the
strong results from the first two vertical holes confirming broad
intervals of lithium-rich mineralization, drilling will continue West
and North through to the end of 2018

*  Falchani West is across a shallow, incised valley cutting down
into, and floored by Li-rich tuff mineralization, located to the west
of the existing Falchani "East" lithium deposit resources

*  The lithium tuff and upper and lower breccia units outcrop on
the Eastern slope at Falchani West and are interpreted as a
continuation of the Falchani East lithium zones

"We have successfully demonstrated our lithium rich units of
mineralization continue West of our maiden resource in the Falchani
East area" commented Alex Holmes, CEO. "Falchani West will be a focus
of drilling until the end of 2018 as this near surface target extends
over a significant footprint and will be part of a resource update in
late Q1 2019."

A fourth rig is now drilling at Falchani East to complete some
infill drilling in areas of inferred resource category.

Drill Results - Details

Platform 14 - Vertical hole collared ~700 m W of Platform 8 from
Falchani East resource drilling PLAT14-V Vertical Hole - 179.0 m total
length

*  65 m of Lithium-rich tuff unit intersected 3,374 ppm Li (0.73%
Li(sub)2(/sub)O) from 9 to 74 m
*  High-grade lithium-rich mineralization in tuff and overlying
upper breccia and a thick ()100 m) intersection of lower breccia
intersected 172 m of 2,908 ppm Li (0.63% Li(sub)2(/sub)O) from 7 to 179
m (EOH)
*  Longest interval of lower breccia unit drilled to date with Li
values up to 4,230   ppm
*  No surface uranium mineralization intersected as hole started
in 7 m of barren rhyolite

Platform 13 - Vertical drill hole collared ~640 m W of Platform 8
from Falchani East Resource drilling PLAT13-V Vertical Hole - 143 m
total length

*  93 m of Lithium-rich tuff unit intersected 2,839 ppm Li (0.61%
Li(sub)2(/sub)O) from 42 to 135 m
*  104 m of 2,728 ppm Li (0.59% Li(sub)2(/sub)O) in broader
interval from 39 to 143 m, that includes Li-rich breccias located above
and below the tuff unit
*  No surface uranium mineralization intersected as hole started
in barren rhyolite

Quality Assurance, Quality Control and Data Verification Drill
core samples are cut longitudinally with a diamond saw with one-half of
the core placed in sealed bags and shipped to Certimin's sample
analytical laboratory in Lima for sample preparation, processing and
ICP-MS/OES multi-element analysis. Certimin is an ISO 9000 certified
assay laboratory. The Company's Qualified Person for the drill
programme, Mr. Ted O'Connor, has verified the data disclosed, including
drill core, sampling and analytical data in the field and lab. The
program is designed to include a comprehensive analytical quality
assurance and control routine comprising the systematic use of Company
inserted standards, blanks and field duplicate samples, internal
laboratory standards and has also included check analyses at other
accredited laboratories.

Qualified Persons Mr. Ted O'Connor, P.Geo., a Director of Plateau
Energy Metals, and a qualified person as defined by National Instrument
43-101 Standards of Disclosure for Mineral Projects, has reviewed and
approved the scientific and technical information contained in this
news release.

Contact Information:

Contact:

//st

Plateau Energy Metals Inc.     Website: www.plateauenergymetals.com

Alex Holmes, CEO & Director    Facebook: www.facebook.com/pluenergy/

+1-416-628-9600                Twitter: www.twitter.com/pluenergy/

info@plateauenergymetals.com

//et

About Plateau Energy Metals Plateau Energy Metals Inc. is a
Canadian lithium and uranium exploration and development company
focused on its properties on the Macusani Plateau in southeastern Peru.
The Company controls all reported uranium resources known in Peru,
significant and growing lithium resources and mineral concessions
covering over 93,000 hectares (930 km2) situated near significant
infrastructure. Plateau Energy Metals is listed on the TSX Venture
Exchange under the symbol 'PLU', quoted on the OTCQB under the symbol
"PLUUF" and the Frankfurt Exchange under the symbol 'QG1'. The Company
has 71,620,208 shares issued and outstanding.

Forward Looking Information This news release includes certain
forward-looking statements concerning possible expected results of
exploration and future exploration and development activities.
Forward-looking statements are frequently identified by such words as
"may", "will", "plan", "expect", "anticipate", "estimate", "intend" and
similar words referring to future events and results. Forward-looking
statements are based on the current opinions and expectations of
management. All forward-looking information is inherently uncertain and
subject to a variety of assumptions, risks and uncertainties, including
risks and uncertainties relating to the interpretation of drill
results, the geology, grade and continuity of mineral deposits; the
possibility that any future exploration, development or mining results
will not be consistent with our expectations; mining and development
risks, including risks related to accidents, equipment breakdowns,
labour disputes (including work stoppages and strikes) or other
unanticipated difficulties with or interruptions in exploration and
development; the potential for delays in exploration or development
activities; risks related to commodity price and foreign exchange rate
fluctuations; risks related to foreign operations; the cyclical nature
of the industry in which we operate; risks related to failure to obtain
adequate financing on a timely basis and on acceptable terms or delays
in obtaining governmental approvals; risks related to environmental
regulation and liability; political and regulatory risks associated
with mining and exploration; risks related to the certainty of title to
our properties; risks related to the uncertain global economic
environment; and other risks and uncertainties related to our
prospects, properties and business strategy, as described in more
detail in Plateau Energy Metals' recent securities filings available at
www.sedar.com. Actual events or results may differ materially from
those projected in the forward-looking statements and Plateau cautions
against placing undue reliance thereon. Neither Plateau nor its
management assume any obligation to revise or update these
forward-looking statements.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1828100041TS11828102390-09171820181009