Source	MARKET NEWS
Date	10/10/2018
Time	05:24:52 AM

Company	 Stratabound Minerals Corp.
Title	Intercepts 60.1 gpt Gold over 0.9 Metre within B





    CDNX Symbol: SB











Press Release





Intercepts 60.1 gpt Gold over 0.9 Metre within Broader 2.53 gpt Goldover 33.1 
Metres from Maiden Drill Program at Golden Culvert, YukonTerritory --->@NEWS 
RELEASE
STRATABOUND MINERALS CORP ("SB-V")
- Intercepts 60.1 gpt Gold over 0.9 Metre within Broader 2.53 gpt
- Gold over 33.1 Metres from Maiden Drill Program at Golden Culvert,
- Yukon Territory

Stratabound Minerals Corp. ("Stratabound" or "the Company") is
pleased to announce the initial results from the first diamond drill
program on Golden Culvert, located in the Hyland-Selwyn gold belt in
the eastern Yukon Territory.  A series of 8 diamond drill holes were
drilled, denoted as GC1801 through GC1808.  Complete assay results have
been returned to date for only holes GC1801, GC1803 and GC1804.  This
press release addresses those holes exclusively.  Diamond drill results
herein are reported down the hole and are not represented here as true
widths.

Drill Hole GC1803

Located 350 metres southeast of the discovery outcrop, drill hole
GC1803 intercepted 2.53 gpt Au over 33.1 metres of quartz breccia,
veining and sulphides between 111.5 and 144.6 metres down the hole.
The intercept includes 60.1 gpt Au over 0.9 metre within a quartz vein
that averages 26.04 gpt Au over 2.5 metres overall.  The quartz vein is
interpreted from surface mapping and trenching to be the 350 metre
strike extension of the Main Vein discovered in 2008 which reported
historic chip samples between 7.7 to 22.8 gpt gold over 1 metre true
width and gold-bearing wallrock grading up to 2.27 gpt Au over 0.5
metre true width.   Photographs of the core and an updated corporate
presentation will be posted on the Company's website at
www.stratabound.com.

Logged core angles confirm the near vertical attitudes of the
controlling gold mineralized quartz vein structures observed from the
surface mapping and trench exposures performed and reported on earlier
this summer.  All primary quartz vein observations conform to the
regional 320 strike structural fabric controlling the encompassing 3
kilometre by 250 metre wide gold-in-soil anomaly.

The high grade Main Vein Zone of breccia and mineralization
intercepted in GC1803 project to surface from 110-130 metres below and
lie directly under the higher grade portion of one of the greater than
200 ppb gold-in-soil anomalies.  Trench TR1805 which intercepted 1.43
gpt Au over 12.0 metres including 4.23 gpt Au over 3.0 metres in a
quartz vein that extends from the Main Vein a further 80 metres
southeast along strike. (Stratabound press release of August 23, 2018).


The Main Vein Zone to date has therefore been traced with
continuous gold mineralization appearing to extend along 450 metres of
strike length, to 130 metres depth below surface and remaining open
along strike and at depth.

Drill hole GC1803 also intersected a second deeper interval of
0.75 gpt Au over 19.5 metres down the hole, also associated with quartz
veining, breccia and sulphides between 226.0 - 235.5 metres ending in
gold mineralization only 3 metres before the end the hole at 238.5
metres.  This intersection is interpreted to be in a second parallel
gold bearing structural zone approximately 50 metres to the southwest
of the Main Vein zone which was intersected in trenches TR1801B and
TR1804.  Trench TR1801B intersected 1.49 gpt Au over 10.0 metres
including 6.11 gpt Au over a 1.5 metre in a quartz vein, and trench
TR1804 intercepted 2.33 gpt Au over 3 metres including 5.32 gpt Au over
1.0 metre in a quartz vein.

Drill Hole GC1801
Drill hole GC1801 was terminated early at 19.8 metres after
intersecting a fault, and returned no significant values.

Drill Hole GC1804

Drill hole GC1804 intercepted 0.51 gpt Au over 9.5 metres between
126.5 - 136 metres down the hole.

All holes for which full assays have been returned to date are
listed in Table 1 below.

Table is available at
https://globenewswire.com/news-release/2018/10/10/1619190/0/en/Stratabound-
Intercepts-60-1-gpt-Gold-over-0-9-Metre-within-Broader-2-53-gpt-Gold-over-3
3-1-Metres-from-Maiden-Drill-Program-at-Golden-Culvert-Yukon-Territory.html




Assay results remain outstanding on the remaining five drill
holes. Summary grades above are reported uncapped as there are
insufficient results returned to date to make a reasonable capping
determination.

Figure 1 is available at:
http://www.globenewswire.com/NewsRoom/AttachmentNg/303821d6-dec7-43fc-80f4-
b37d1ac39578

Figure 2 is available at:
http://www.globenewswire.com/NewsRoom/AttachmentNg/2c389857-6f39-4252-934a-
c0ebbc78b13b

President and CEO, R. Kim Tyler commented, "We have had an
exceptional first field season at Golden Culvert and are extremely
pleased with our results to date.  The high grade 60.1 gpt gold
intercept and the broader low grade gold around it in hole GC1803
confirm what we have learned from our mapping, trenching and previous
historical work; that a vertically dipping structural corridor of
gold-bearing quartz veins, quartz breccia and sulphide mineralization
can be traced over 450 metres of strike; 130 metres deep so far and
remaining open both along strike and depth.  We have only focused on a
small 800 metre segment of the larger 24 kilometres of prospective
strike length within our property option.  We are expecting further
results in the near future, and as the hole assay results are returned
and analyzed they will be reported in separate press releases."

Analytical, QA/QC Methods and Protocol:

All trench and drill core samples were delivered to the ALS Global
preparation facility in Whitehorse, Yukon Territory where they were
crushed to 70% passed a 2mm sieve, then a 250g split was pulverized
until better than 85% passed a 75 micron screen. Gold was tested by a
30 gram fire assay method with an atomic absorption finish at the
Vancouver ALS lab facility. Assay results that exceed 100 gpt Au by
this method are re-assayed by fire assay with a gravimetric finish.  In
addition to the quality assurance and quality control program performed
by ALS, Stratabound personnel insert internationally certified
standards and field blanks into the sample stream at the rate of one
QA/QC sample for every 15 samples and maintain a program of duplicate
sampling on pulp rejects.

About the Golden Culvert and Little Hyland Properties

Golden Culvert and Little Hyland cover 83.8 square kilometres in
the southeast Yukon Territory across a 24-kilometre strike located
approximately 20 kilometres northeast of and parallel to Golden
Predator Mining Corp.'s 3 Aces property.  Work filed in Yukon mineral
claims assessment reports has outlined a northerly trending, 3
kilometre by 250 metre, +30 ppb Au up to 791 ppb Au gold-in-soil
anomaly that remains open at both ends.  The soil anomaly is centred
around partially exposed primary gold-bearing quartz veins grading
between 7.7 to 22.8 gpt gold over 1 metre and complimentary
gold-bearing quartz vein stockwork within a larger silicified, altered,
sulphide and gold-bearing wallrock grading up to 2.27 gpt gold over 0.5
metre.

Trench samples on six trenches completed earlier this summer have
been reported on in Stratabound's press release dated August 23, 2018.
Prior to this summer's trenching and drilling 3,645 soil samples, 48
stream samples, 239 rock samples, 19.4 line-km of ground magnetic
survey and 18.5 line-km of VLF survey had been taken at the property.
This summer's program of $0.75 million includes the completed trenching
and drilling to further explore the highly mineralized areas of the
property.

About Stratabound

Stratabound Minerals Corp. is a Canadian exploration and
development company focused on the Yukon Territory.  The Company also
holds a significant land position that hosts three base metals deposits
in the Bathurst base metals camp of New Brunswick featuring the Captain
Copper-Cobalt Deposit that hosts an NI 43-101 Measured+Indicated
resource.

Stratabound management has a diversified track record of
exploration, development and operating successes that will facilitate
the development of the Company's exploration projects. Mr. R. Kim
Tyler, P.Geo., President and CEO of Stratabound, and a "Qualified
Person" for the purpose of NI 43-101, was responsible for managing and
supervising the exploration program and has verified the data
disclosed, including sampling, analytical, and test data underlying the
information or opinions contained in this disclosure.  Mr. Tyler has
reviewed and approved the contents of this news release.

For further information, please see the Golden Culvert
presentation and the NI 43-101 technical report on the Stratabound web
site, www.stratabound.com.

For further information

Contact Information:
contact:

R. Kim Tyler, President and CEO 705-822-9771
ktyler@stratabound.com

Ritu Gupte, Investor Relations Consultant 647-267-5380
rgupte@stratabound.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

WARNING: the Company relies upon litigation protection for
"forward looking" statements. The information in this release may
contain forward-looking information under applicable securities laws.
This forward-looking information is subject to known and unknown risks,
uncertainties and other factors that may cause actual results to differ
materially from those implied by the forward-looking information.
Factors that may cause actual results to vary materially include, but
are not limited to, inaccurate assumptions concerning the exploration
for and development of mineral deposits, currency fluctuations,
unanticipated operational or technical difficulties, changes in laws or
regulations, failure to obtain regulatory, exchange or shareholder
approval, the risks of obtaining necessary licenses and permits,
changes in general economic conditions or conditions in the financial
markets and the inability to raise additional financing. Readers are
cautioned not to place undue reliance on this forward-looking
information. The Company does not assume the obligation to revise or
update this forward-looking information after the date of this release
or to revise such information to reflect the occurrence of future
unanticipated events, except as may be required under applicable
securities laws.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1828200003TS11828200741-05221120181010