Source	MARKET NEWS
Date	10/10/2018
Time	12:55:39 PM

Company	 Jaxon Mining Inc.
Title	Completion Of 
First Diamond Drill Hole On Backbo





    CDNX Symbol: JAX











Press Release





JAXON MINING INC ("JAX-V")
- Completion Of First Diamond Drill Hole On Backbone Gold-Bearing
- Tourmaline Breccia Zone At Its Red Springs Project

Jaxon Mining Inc. is pleased to announce completion of its first
diamond drill hole, BB18-01, as part of its Phase One diamond drilling
program on the Backbone gold-bearing tourmaline breccia zone at its Red
Springs project. Red Springs is located on part of Jaxon's
44,000-hectare Hazelton property in the Skeena Arch area of northwest
British Columbia, Canada.

Drilling Program Highlights:

BB18-01, a diamond drill hole with HQ core (63.5 mm in diameter),
has now been completed to a depth of 148 metres with a dip angle of -50
degrees.

BB18-01 intercepts the gold-bearing tourmaline breccia zone from a
depth of 18 metres to 35 metres, which includes 6 metres of strongly
silicified and sulphide mineralization from 20 metres to 26 metres
(Pictures 1 to 3, below).

BB18-01 confirms the dip extension of the high-grade gold-bearing
tourmaline breccia mineralization at the Channel A outcrop, which has
reported a channel sample with a gold grade of up to 6.57 grams per
tonne (g/t), 1.35% copper and 0.04% cobalt.

Drilling has commenced on the second drill hole, BB18-02, with a
dip angle of -85 degrees to test the IP chargeability anomaly which are
interpreted to be associated with sulphide mineralization (Figure 2,
below), using the same drill pad and azimuth as BB18-01.

Picture 1 - a segment of strong sulphided (Pyrite and
Arsenopyrite) tourmalization breccia mineralization core at 25.80
metres from drill hole BB18-01 at Jaxon's Red Springs project.

To view an enhanced version of Picture 1, please visit:
http://orders.newsfilecorp.com/files/881/40262_a1539143604227_60.jpg

Picture 2 - a segment of strong sulphided (Pyrrhotite and
Arsenopyrite) tourmalization breccia mineralization core at 21.20
metres from drill hole BB18-01 at Jaxon's Red Springs project.

To view an enhanced version of Picture 2, please visit:
http://orders.newsfilecorp.com/files/881/40262_a1539143604352_40.jpg

Picture 3 - drill cores from 17.4 metres to 26.7 metres at drill
hole BB18-01 at Jaxon's Red Springs project, exhibiting very strong
silicified and sulphide mineralization.

To view an enhanced version of Picture 3, please visit:
http://orders.newsfilecorp.com/files/881/40262_a1539143604759_83.jpg

Tony Guo, Jaxon's COO, commented: "We are encouraged that we have
intercepted a very strong silicified and sulphide tourmaline breccia
zone with a reasonable thickness at our first drill hole, BB18-01. We
are expecting our second drill hole to confirm this tourmaline breccia
zone again and also test a moderate IP chargeability anomaly at a depth
of 150 to 200 metres in the Backbone area."

About Jaxon's Red Springs Drilling Program

Jaxon's Phase One of a 2,000 to 2,200-metre diamond drilling
program consists of eight drill holes on the Backbone gold-bearing
tourmaline breccia zone. Drilling commenced October 4th of 2018 and is
due to be completed by the end of October 2018.

The Backbone gold-bearing tourmaline breccia zone target has a
1000-metre long strike with up to 15-metre-width outcrops on surface,
(Figure 1, below). This zone, per previously released assay results,
indicates the mineralization existence of high-grade gold of up to
25.86 g/t with cobalt, copper, antimony and silver credits.

The objective of the Phase One drilling program is to determine
the width, continuity and grade of gold-bearing tourmaline breccia
mineralisation at depth. A further objective is to demonstrate the
viability of IP geophysics as an exploration tool for the
mineralisation at the Red Springs project and will provide the
opportunity for further down-hole geophysics to better define the
geometry of any mineralisation intersected during the program (Figure
2). In addition, it is anticipated that the results will add to Jaxon's
knowledge of the nature of the tourmaline breccia mineralisation and
its controls.

The Company will provide further information as it becomes
available and will release updates on the progress of drilling over the
coming weeks, including posting videos and photos on its website at
www.jaxonmining.com.

Figure 1 - Backbone high grade gold-bearing tourmaline breccia
zone at the Red Springs project.

To view an enhanced version of Figure 1, please visit:
http://orders.newsfilecorp.com/files/881/40262_a1539143605040_15.jpg

Figure 2 - 2D resistivity and 2D IP chargeability anomalies at
Backbone tourmaline breccia zone.

To view an enhanced version of Figure 2 , please visit:
http://orders.newsfilecorp.com/files/881/40262_a1539143605431_65.jpg

Qualified Person

Yingting (Tony) Guo, P.Geo., COO for Jaxon Mining Inc., a
Qualified Person as defined by National Instrument 43-101, has reviewed
the drilling program, prepared the scientific and technical information
and verified the data supporting such scientific and technical
information contained in this news release.

About Jaxon Mining Inc.

Jaxon is a precious and base metals exploration company with a
regional focus on Western Canada. The Company is currently focused on
advancing its Hazelton Project in north-central British Columbia and
the More Creek Project (consolidating the Wishbone and Foremore
properties) in British Columbia's Golden Triangle.

ON BEHALF OF THE BOARD OF DIRECTORS
JAXON MINING INC.
"John King Burns"
John King Burns, Chairman

For Head of Capital Markets for Jaxon Mining Inc., please call
778-938-4459, for Investor Relations enquiries, please call
604-609-6152, and for Corporate enquiries, please call 604-608-0400, or
Toll free: 1-877-608-0007.

This news release may contain forward-looking information, which
is not comprised of historical facts. Forward-looking information
involves risks, uncertainties and other factors that could cause actual
events, results, performance, prospects and opportunities to differ
materially from those expressed or implied by such forward-looking
information. Forward-looking information in this news release may
include, but is not limited to, the Company's objectives, goals or
future plans. Factors that could cause actual results to differ
materially from such forward-looking information include, but are not
limited to, those risks set out in the Company's public documents filed
on SEDAR. Although the Company believes that the assumptions and
factors used in preparing the forward-looking information in this news
release are reasonable, undue reliance should not be placed on such
information, which only applies as of the date of this news release,
and no assurance can be given that such events will occur in the
disclosed time frames, or at all. The Company disclaims any intention
or obligation to update or revise any forward-looking information,
whether as a result of new information, future events or otherwise,
other than as required by law. Neither TSX Venture exchange nor its
Regulations Services Provider (as that term is defined in the policies
of the TSX Venture Exchange) accepts responsibility for the adequacy or
accuracy of this release.

TEL:  778-938-4459
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1828200059TS11828202589-12520220181010