Source	MARKET NEWS
Date	09/12/2018
Time	06:45:45 AM

Company	 Altus Strategies Plc
Title	Exploration Update on High Grade Bikoula Iron Or





    CDNX Symbol: ALTS











Press Release





Exploration Update on High Grade Bikoula Iron Ore Project, SouthernCameroon 
--->@NEWS RELEASE
ALTUS STRATEGIES PLC ("ALTS-V")
- Exploration Update on High Grade Bikoula Iron Ore Project, Southern
- Cameroon

Altus Strategies Plc, the Africa focused exploration project
generator, provides an update on exploration activities at its 97.3%
owned 400km(sup style="text-align: left;")2 Bikoula and Ndjele high
grade colluvial iron ore project ("Bikoula" or the "Project") in
southern Cameroon.

Highlights:

*  Reconnaissance pitting and mapping confirms additional
supergene haematite
*  Historic drilling results include 57.8m @ 51.4% Fe (incl. 30.8m
at 57.9% Fe from 3.8m)
*  Previous metallurgical testing by SGS has yielded a 62.7% Fe
concentrate from gravity separation
*  Project strategically located close to existing road and
potential rail line to Kribi deep sea port

Steven Poulton, Chief Executive of Altus, commented:

"High grade iron ore products are currently yielding significant
premiums to general market prices. Our Bikoula project is located
within a strategic iron ore corridor in southern Cameroon and hosts a
high grade unconsolidated colluvial and haematite weathered blanket,
above a primary magnetite orebody. As previously reported, preliminary
metallurgical test-work on representative samples from Bikoula have
yielded a 62.7% Fe concentrate from gravity separation alone.

"In light of the potential high quality ore and the Project's
strategic location, our exploration team has recently completed a
reconnaissance pitting and mapping programme at Bikoula. The pitting
programme has successfully confirmed the presence of clasts of
supergene oxidised banded iron, indicating that the colluvial iron ore
body continues along strike into these areas. We look forward to
updating shareholders on our progress in due course".

Exploration programme

A programme of reconnaissance geological mapping and pitting has
been completed over two previously untested magnetic anomalies at
Bikoula. Surface mapping has identified oxidised supergene magnetite
banded iron formation ("BIF") as well as haematite colluvium. Five hand
dug pits, each up to 5m depth, have been excavated and logged. Mapping
of the pit walls has revealed a number of oxidised and highly weathered
BIF clasts, within an iron rich matrix.

Previous results
The 200km2 Bikoula and adjacent 200km2 Ndjele licences were
selected based on the presence of significant magnetic anomalies that
are coincident with historically mapped BIFs. The BIFs form the
westerly strike extension of the Nkout iron ore deposit. A high
resolution airborne magnetic survey completed by the Company identified
three priority prospect areas.

Follow up pitting and drilling on the first prospect area has
defined a historic maiden JORC (The Australasian Code for Reporting of
Exploration Results, Mineral Resources and Ore Reserves) Inferred
Mineral Resource (see Table 1.). The resource statement is not in
accordance with NI 43-101. The independent resource report was prepared
by Coffey Mining South Africa (Pty) Ltd and is entitled 'Mineral
Resource Estimation and Classification of the Bikoula Iron Ore Project
in Cameroon' and is dated April 2014. The non-43-101 resource was
calculated on less than 25% of the strike of a 17km long airborne
geophysical target.

48 diamond drill holes, totalling approximately 3,900m, have been
drilled to date at Bikoula. Over half of the holes have intersected at
least 20m of )40% Fe. Significant intersections include:

*  57.8m @ 51.4% Fe (including 30.8m at 57.9% Fe, from 3.8m)
*  35.0m @ 55.9% Fe from 10.0m
*  28.3m @ 49.9% Fe from 15.0m

The Bikoula project comprises a blanket of colluvial haematite,
which is typically 200-300m wide and reaches up to 500m wide in places.
The blanket is located at surface and is typically up to 9.8m deep, up
to 23.7m based on drill hole logging. In places it rests directly above
a horizon of supergene enriched haematite which in turn sits above a
significant BIF formation. The BIF has yielded average grades of 39.0%
Fe ('Oxide BIF') and 34.1% Fe ('Fresh BIF'). The Oxide BIF and Fresh
BIF do not form part of the historic non-43-101 mineral resource
estimate.

Table 1: Historic JORC Inferred Mineral Resource Estimate
(non-43-101) dated April 2014 (non-beneficiated)

//st

Zone    Rock Type   Tonnage   Fe     SiO2   P      TiO2   Al2O3   S      LOI
(Mt)      (%)    (%)    (%)    (%)    (%)     (%)    (%)

Libi    Colluvium   39        43.0   13.1   0.09   0.8    14.8    0.04   9.3
North

Supergene   5         52.7   14.3   0.07   0.7    5.1     0.02   4.1

Lombo   Colluvium   1         43.6   22.0   0.09   0.4    8.1     0.03   6.2

Supergene   1         38.9   35.3   0.08   0.2    4.4     0.02   3.4

Total               46        44.2   13.9   0.08   0.7    13.4    0.03   8.5

//et

Notes: No Geological loss and cut-off are considered.

Estimate is reported in accordance with the JORC Code 2012.

Metallurgical test work results

Previous metallurgical test-work undertaken on bulk samples from
Bikoula have indicated that processing using simple cost effective
methods may produce a significant high grade product. A bulk composite
sample, weighing 177kg, of colluvial material was historically
collected from a series of 3-5 m deep pits and processed by Bureau
Veritas in Perth, Australia. A simple gravity separation circuit
yielded a concentrate of 62.26% Fe, with reduced levels of
contaminants, including 2.7% SiO (sub)2(/sub) and 3.8%
Al(sub)2(/sub)O(sub)3(/sub), produced at a mass recovery of 43.2%. In
addition, a second bulk sample, totalling 129kg, collected from the
friable supergene ore was processed by SGS in Truro, United Kingdom.
The SGS sample had a head grade of 55.55% Fe, 12.98% SiO(sub)2(/sub)
and 3.08% Al(sub)2(/sub)O(sub)3(/sub) from which, when crushed to
-6.35mm and screened, yielded a 62.7% Fe product with 5.4%
SiO(sub)2(/sub) and 2.7% Al(sub)2(/sub)O(sub)3(/sub).

The following figures have been prepared and relate to the
disclosures in this announcement and are visible in the version of this
announcement on the Company's website (www.altus-strategies.com) or in
PDF format by following this link:
www.altus-strategies.com/site/assets/files/4447/bikoula_sep_18.pdf

*  The location of Bikoula in Southern Cameroon is shown in Figure
1.
*  An overview of the Bikoula & Ndjele licences is shown in Figure
2.
*  An overview of the historic (non 43-101) mineral resource
estimate is shown in Figure 3.
*  A schematic geological cross-section through the Bikoula
deposit is shown in Figure 4.
*  A selection of photographs from the recent exploration
programme are shown in Figure 5.

Figure 1. The location of Bikoula in Southern Cameroon

Figure 2. An overview of the Bikoula & Ndjele Licence

Figure 3. An overview of the licence and historic (non 43-101)
mineral resource estimate

Figure 4. A schematic geological cross-section through the Bikoula
deposit

Figure 5. Selection of photographs from the recent exploration
programme

Bikoula Project: Location

The 200km 2 Bikoula licence and contiguous 200km2 Ndjele licence
are located in southern Cameroon, approximately 150km southeast of the
capital city of Yaounde. The licences are accessible via a network of
paved and lateritic roads which also connect the Project to the newly
constructed deep water port at Kribi. Bikoula is situated within 30km
from a proposed trans-Cameroon railway line that aims to service a
number of iron ore deposits in the region, including Mbalam and Nkout,
the latter of which is located directly along strike of the Project.

Bikoula Project: Geological setting

The Bikoula and Ndjele licences were selected based on the
presence of significant magnetic geophysical signatures. The Project
area is underlain by the Ntem Unit of the Archaean Ntem Complex which
is comprised of two main 'series'; an intrusive group comprising
tonalities and granodiorites, as well as a banded group made up of
deformed granulitic gneisses. In addition, the complex hosts a number
of discontinuous greenstone belts that are typically sheared and
faulted, containing paragneisses, amphibolites, pyroxenites and banded
iron formations.

Within the licences, metasedimentary rocks represent an
interbedded sequence of exhalative chemical sediments and clastic units
which weather near surface and grade into primary banded iron
formations at depth. These steeply dipping iron-rich units trend along
an approximately NW-SE strike and are sporadically cut by a number of
E-W and NE-SW trending faults. Colluvial iron mineralisation comprises
a blanket of unconsolidated weathered supergene BIF clasts, with grains
of oxidised magnetite and depleted levels of silica. The colluvial
material; is usually found as a layer of variable thickness above the
BIFs.

Qualified Person

The technical disclosure in this regulatory announcement has been
read and approved by Steven Poulton, Chief Executive of Altus. A
graduate of the University of Southampton in Geology (Hons), he also
holds a Master's degree from the Camborne School of Mines (Exeter
University) in Mining Geology. He is a Fellow of the Institute of
Materials, Minerals and Mining and has over 19 years of experience in
mineral exploration and is a Qualified Person under the AIM rules and
National Instrument 43-101 under the rules of the TSX.

Market Abuse Regulation (MAR) Disclosure

Certain information contained in this announcement would have been
deemed inside information for the purposes of Article 7 of Regulation
(EU) No 596/2014 until the release of this announcement.

For further information you are invited to visit the Company's
website www.altus-strategies.com or contact:

//st

Altus Strategies Plc Steven            Tel: +44 (0) 1235 511 767 E:
Poulton, Chief Executive

SP Angel (Nominated Adviser)           Tel: +44 (0) 20 3470 0470
Richard Morrison / Soltan Tagiev

SP Angel (Broker) Richard Parlons /    Tel: +44 (0) 20 3470 0471
Jonathan Williams

Blytheweigh (Financial PR) Tim         Tel: +44 (0) 20 7138 3204
Blythe / Camilla Horsfall / James
Husband

//et

About Altus Strategies Plc

Altus is a London (AIM: ALS) and Toronto (TSX-V: ALTS) listed,
diversified and Africa focused mineral exploration project generator.
Through our subsidiaries we discover new projects and attract third
party capital to fund their growth, development and ultimately exit
optionality. This strategy enables Altus to remain focused on the
acquisition of new opportunities to be fed into the project generation
cycle and aims to minimise shareholder dilution. Our business model is
designed to create a growing portfolio of well managed and high growth
potential projects and royalties, diversified by commodity and by
country. Altus currently has eighteen projects in six commodities
across six countries. We aim to position our shareholders at the
vanguard of value creation, but with significantly reduced risks
traditionally associated with investments in the mineral exploration
sector.

Cautionary Note Regarding Forward-Looking Statements

Certain statements in this news release contain forward-looking
information. These statements address future events and conditions and,
as such, involve known and unknown risks, uncertainties and other
factors which may cause the actual results, performance or achievements
to be materially different from any future results, performance or
achievements expressed or implied by the statements. Such factors
include without limitation the completion of planned expenditures, the
ability to complete exploration programs on schedule and the success of
exploration programs. Readers are cautioned not to place undue reliance
on the forward-looking information, which speak only as of the date of
this news release.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Glossary of Terms "BIF" means Banded Iron Formation

"DSO" means Direct Shipping Ore

"Gt" means giga tonnes

"km" means kilometres

"km2" means square kilometres

"Mt" means million tonnes
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1825400032TS11825401156-06405820180912