Source	MARKET NEWS
Date	10/17/2007
Time	03:53:12 AM

Company	 Largo Resources Ltd.
Title	Drilling 
Confirms Extensive Vanadium PGM DepositAt Largo's Maracas Project (Brazil)





    CDNX Symbol: LGO











Press Release	




[200/News Release]LGOVLARGO RESOURCES LTDOCT 17 2007  04:52 AMDrilling 
Confirms Extensive Vanadium PGM DepositAt Largo's Maracas Project (Brazil) 
--->@NEWS RELEASELARGO RESOURCES LTD  ("LGO-V")
- Drilling Confirms Extensive Vanadium-PGM Deposit
- At Largo's Maracas Project (Brazil)

Largo Resources Ltd. is pleased to provide a further update on its
exploration program in progress on the Company's 2,000 hectare Maracas
Vanadium-PGM property located 250 kilometres west of Salvador, Bahia,
Brazil.

To date, 45 diamond drill holes totalling 11,196 metres have been
completed on the Gulcari "A" deposit in order to expand and upgrade the
Vanadium-PGM mineralization and the previously announced inferred mineral
resource of 15.0 million tonnes grading 1.37% Vanadium Pentoxide (V2O5)
(see press release November 22, 2006). Results were previously released for
16 holes (see press releases May 22, 2007, June 19, 2007 and July 18 2007).
Three holes were drilled for geotechnical and metallurgical purposes
(FGA81, FGA84 and FGA85). Significant results for the remaining 26 holes
are summarized in Table 1.

Highlights from the new results include:

- FGA73 - 40.0 metres true width at 1.62% V2O5 and 0.34 g PGM/t (0.24 g
Pt/t and 0.10 g Pd/t) and 17.5 metres true width at 2.81% V2O5 and 0.59 g
PGM/t (0.54 g Pt/t and 0.05 g Pd/t)

- FGA74 - 39.0 metres true width grading 1.86% V2O5 and 0.27 g PGM/t
(0.24 g Pt/t and 0.03 g Pd/t) including 25.0 metres true width grading
2.15% V2O5, and 0.25 g PGM/t (0.21 g Pt/t and 0.04 g Pd/t)

- FGA77 - 17.9 metres true width grading 2.37% V2O5, and 0.25 g PGM/t
(0.22 g Pt/t and 0.03 g Pd/t))

- FGA79 - 70.0 metres true width grading 1.60% V2O5, and 0.32 g PGM/t
(0.26 g Pt/t and 0.06 g Pd/t)) including 38.0 metres true width grading
2.32% V2O5, and 0.43 g PGM/t (0.35 g Pt/t and 0.08 g Pd/t)

- FGA87 - 22.0 metres true width grading 1.82% V2O5, and 0.41 g PGM/t
(0.19 g Pt/t and 0.22 g Pd/t))

- FGA89 - 59.0 metres true width grading 2.11% V2O5, and 0.26 g PGM/t
(0.19 g Pt/t and 0.07 g Pd/t)) including 36.0 metres true width grading
2.40% V2O5 and 0.27 g PGM/t (0.20 g Pt/t and 0.07 g Pd/t)

- FGA95 - 65.0 metres true width grading 1.46% V2O5, and 0.21 g PGM/t
(0.11 g Pt/t and 0.10 g Pd/t))

- FGA97 - 50.3 metres true width grading 1.83% V2O5, and 0.47 g PGM/t
(0.28 g Pt/t and 0.19 g Pd/t)) including 29.3 metres true width grading
2.26% V2O5, and 0.50 g PGM/t (0.34 g Pt/t and 0.16 g Pd/t)

Andy Campbell, P.Geo., Vice President Exploration commented: "Of the 42
holes drilled to expand and upgrade the resource, only one hole did not
intersect the magnetite-rich layer confirming the excellent continuity of
the Gulcari "A" deposit. Twenty of the 42 holes returned intersections that
significantly exceeded the average grade (1.35% V2O5) and average true
width (25m) of the original deposit. The deposit, which now extends 400m
along strike and to a depth of 300m, is still open along strike as well as
at depth."

Largo President & CEO Mark Brennan commented: "We are delighted with
the results of the drilling program which have exceeded expectations. The
updated resource estimate, which is in progress, will form the basis for an
expanded scoping study including PGMs. Engineering work on the metallurgy
is also well advanced."

PGM Exploration

The Gulcari "A" deposit is part of a mineralizing system that extends
for 8 kilometres across the property. Results from drilling of the deposit
indicate that the PGM mineralization is related to the disseminated
sulphides in the massive magnetite zone. The PGM mineralization is
significant and consistent throughout the massive magnetite lens with a
very high Pt:Pd ratio averaging about 4:1, which is a comparable ratio to
the Great Dyke. Of particular interest is Hole FGA-80 which intersected
3.93 g Pt/t and 0.21 g Pd/t (4.14 g PGM/t) over 1.0m in a section with 3-7%
sulphides but very low magnetite. This suggests in addition to the
magnetite lens, there is excellent potential for outlining higher grade PGM
mineralization that may not be directly associated with magnetite.

With drilling on the main deposit complete, exploration has now shifted
focus to test other areas along the system including, from north to south,
Nova Amparo, Sao Jose and Gulcari "B". Eleven (11) shallow drill holes
totalling 1,952 metres have now been completed at Nova Amparo located 4 km
to the north of Gulcari "A" to test for PGMs associated with a magnetite
lens. The initial indications from this drilling are that there are more
sulphides associated with the magnetite at Nova Amparo compared to Gulcari
"A". Assay results are pending for these holes.

Additional work in progress includes geological mapping at a scale of
1:2,500 and geophysical (magnetics and induced polarization (IP)) surveys.
The magnetic survey has been completed while the IP survey is approximately
60% complete and is expected to be finished in early November. The
geophysical work is being directed by Dr. Chris Hale, P.Geo., consulting
geophysicist and a Qualified Person as defined under NI 43-101.

Analytical work was carried out by SGS Minerals in Belo Horizonte,
Brazil, an ISO 9001-2000 certified laboratory. Largo employs a systematic
industry standard QA/QC program including standards, duplicates and blanks.
Andy Campbell, P. Geo., Largo's Vice President of Exploration, is the
Qualified Person responsible for the scientific and technical work for the
program as defined under National Instrument 43-101 and has reviewed this
press release.

About Largo

Largo Resources is a Canadian natural resource development and
exploration company with two advanced stage projects: the Northern Dancer
Tungsten-Molybdenum deposit in the Yukon and the Maracas Vanadium-PGM
deposit in Brazil. Largo also has a large (60,000 hectare) land position
and prospective gold exploration properties in Ecuador. The company is
listed on the TSX Venture Exchange under the symbol LGO.

For more information please refer to Largo's website:
www.largoresources.com.

Disclaimer

Statements in this release that are not historical facts are
"forward-looking statements" within the meaning of applicable securities
laws. Readers are cautioned that any such statements are not guarantees of
future performance and those actual developments or results may vary
materially from those in these "forward-looking statements".



//st

Table 1: Summary of Significant Assay Results - Maracas Property, Brazil

---------------------------------------------------------------------
Hole        From     To V2O5     Pt      Pd   PGM  Interval     True
Number                     %   (g/t)   (g/t) (g/t)  (metres)   thick
-ness
(m)
---------------------------------------------------------------------
FGA72     211.55 224.60 1.30   0.12    0.08  0.20     13.05     12.0
and 229.90 239.15 1.43   0.13    0.11  0.24      9.25      9.0
and 249.15 268.15 1.06   0.04    0.05  0.09     19.00     18.0
---------------------------------------------------------------------
FGA73     128.60 148.00 2.81   0.54    0.05  0.59     19.40     17.5
and 151.46 195.46 1.62   0.24    0.10  0.34     44.00     40.0
---------------------------------------------------------------------
FGA74     136.38 175.38 1.86   0.24    0.03  0.27     39.00     39.0
including 148.38 173.38 2.15   0.21    0.04  0.25     25.00     25.0
---------------------------------------------------------------------
FGA75     181.00 216.89 1.19   0.05    0.04  0.09     35.00     35.0
---------------------------------------------------------------------
FGA76      89.00 118.00 1.43   0.08    0.06  0.14     29.00     29.0
including 105.00 118.00 1.93   0.09    0.08  0.17     13.00     13.0
and 128.00 135.00 1.32   0.06    0.08  0.14      7.00      7.0
---------------------------------------------------------------------
FGA77     127.50 145.42 2.37   0.22    0.03  0.25     17.92     17.9
---------------------------------------------------------------------
FGA78     106.95 117.40 0.68   0.08    0.07  0.15     10.45      9.0
---------------------------------------------------------------------
FGA79     148.75 221.00 1.60   0.26    0.06  0.32     72.25     70.0
including 150.00 191.00 2.32   0.35    0.08  0.43     41.00     38.0
---------------------------------------------------------------------
FGA80      22.00  23.00 0.38   3.93    0.21  4.14      1.00      1.0
and  83.70  90.70 0.69   0.07    0.04  0.11      7.00      7.0
and  94.70  98.70 1.02   0.09    0.11  0.20      4.00      4.0
and 114.10 118.10 1.22   0.09    0.08  0.17      4.00      4.0
---------------------------------------------------------------------
FGA82                   No significant results
---------------------------------------------------------------------
FGA83     134.00 152.93 1.77   0.23    0.21  0.44     18.93     18.9
including 139.00 152.93 1.99   0.26    0.25  0.51     13.93     13.9
and 159.72 172.72 1.18   0.05    0.06  0.11     13.00     13.0
---------------------------------------------------------------------
FGA86     178.50 191.16 1.43   0.01    0.02  0.03     12.66     10.0
and 241.00 247.45 1.45   0.19    0.14  0.33      6.45      5.0
and 259.00 265.00 1.28   0.06    0.02  0.08      6.00      5.0
and 276.00 298.00 1.54   0.33    0.19  0.52     22.00     20.0
---------------------------------------------------------------------
FGA87     244.50 259.83 1.93   0.16    0.21  0.37     15.33     15.3
and 267.00 289.00 1.82   0.19    0.22  0.41     22.00     22.0
and 306.00 323.00 0.86   0.05    0.06  0.11     17.00     17.0
---------------------------------------------------------------------
FGA88     177.10 183.10 1.02   0.13    0.10  0.23      6.00      6.0
and 303.10 308.10 1.07   0.25    0.16  0.41      5.00      5.0
---------------------------------------------------------------------
FGA89     297.00 356.00 2.11   0.19    0.07  0.26     59.00     59.0
including 302.00 338.00 2.40   0.20    0.07  0.27     36.00     36.0
---------------------------------------------------------------------
FGA90     279.00 293.00 1.05   0.09    0.07  0.16     14.00     14.0
---------------------------------------------------------------------
FGA91     285.60 294.60 1.32   0.21    0.10  0.31      9.00      9.0
---------------------------------------------------------------------
FGA92     249.00 270.00 0.99   0.07    0.05  0.12     21.00     21.0
---------------------------------------------------------------------
FGA93     264.00 278.00 1.94   0.24    0.18  0.42     14.00     14.0
and 299.00 309.00 1.31   0.10    0.07  0.17     10.00     10.0
---------------------------------------------------------------------
FGA94     204.50 242.12 1.44   0.09    0.05  0.14     37.62     35.0
and 269.00 281.00 1.12   0.08    0.05  0.13     12.00     10.0
---------------------------------------------------------------------
and 292.47 298.00 1.28   0.07    0.06  0.13      5.53      5.0
---------------------------------------------------------------------
FGA95     268.80 336.00 1.46   0.11    0.10  0.21     67.20     65.0
including 268.80 284.60 2.24   0.09    0.09  0.18     15.80     15.8
---------------------------------------------------------------------
FGA96     283.84 290.00 0.81   0.08    0.04  0.12      6.16      6.1
---------------------------------------------------------------------
FGA97     142.73 193.00 1.83   0.28    0.19  0.47     50.27     50.2
including 143.73 173.00 2.26   0.34    0.16  0.50     29.27     29.2
and 218.00 228.00 1.40   0.30    0.30  0.60     10.00     10.0
---------------------------------------------------------------------
FGA98     175.00 187.00 0.80   0.20    0.06  0.26     12.00     12.0
---------------------------------------------------------------------
FGA99     224.00 233.00 1.38   0.10    0.11  0.21      9.00      9.0
and 237.00 241.00 1.55   0.06    0.04  0.10      4.00      4.0
---------------------------------------------------------------------




Drill hole Information - Maracas Property, Brazil

-----------------------------------------------------------
Hole Number    Northing    Easting Elevation Azimuth    Dip
-----------------------------------------------------------
FGA 72        8,486,020    318,336    296.00     290    -45
FGA 73        8,486,130    318,435    299.00     290    -50
FGA 74        8,486,130    318,435    299.00     290    -80
FGA 75        8,486,033    318,288    293.99     290    -45
FGA 76        8,486,011    318,281    293.68     290    -55
FGA 77        8,486,145    318,429    297.82     290    -60
FGA 78        8,486,000    318,320    295.64     290    -65
FGA 79        8,486,133    318,478    300.03     290    -60
FGA 80        8,485,941    318,301    294.70     290    -60
FGA 82        8,486,201    318,926    298.99     290    -60
FGA 83        8,486,065    318,380    298.05     290    -65
FGA 86        8,486,048    318,432    302.00     290    -65
FGA 87        8,486,079    318,523    305.00     290    -65
FGA 88        8,486,055    318,479    309.00     290    -65
FGA 89        8,486,051    318,620    304.00     290    -65
FGA 90        8,485,993    318,498    309.00     290    -65
FGA 91        8,486,106    318,594    300.00     290    -60
FGA 92        8,485,991    318,430    301.00     290    -60
FGA 93        8,486,007    318,530    304.00     290    -65
FGA 94        8,485,968    318,412    301.00     290    -65
FGA 95        8,486,068    318,567    301.41     290    -65
FGA 96        8,486,129    318,531    304.10     290    -60
FGA 97        8,486,130    318,435    298.00     290    -65
FGA 98        8,486,020    318,402    296.00     290    -73
FGA 99        8,485,955    318,465    302.00     290    -65
-----------------------------------------------------------
//et



THE TSX VENTURE EXCHANGE DOES NOT ACCEPT RESPONSIBILITY FOR THE ADEQUACY OR
ACCURACY OF THIS RELEASE.

Capitalization Report for Largo Resources Ltd
Shares Issued: 63260282
Shares Escrow: 0


TEL:  (416) 861-5886   Largo Resources Ltd.
Mark Brennan, President & CEO
Email: mbrennan@largoresources.com

TEL:  (416) 861-5882   Largo Resources Ltd.
Tony LaMantia, VP, Corporate Development
Email: tlamantia@largoresources.com
Website: www.largoresources.com
______________________________
___________________________________________________________________
(c) Market News Publishing Inc.  Tel:(604) 689-1101
All rights reserved.         Fax:(604) 689-1106

071017EA+2+000134